## Slide 1: Distributed Systems 2. Protocol Hierarchies, OSI and TCP/IP
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2015/2016

## Slide 2
Lab groups
Exam language

## Slide 3: Overview
So far: What are applications and paradigms for distributed systems
Today: What are networks composed of
Network Hardware
Network Software/Protocols
  Interfaces/Layers
  OSI
  Internet and TCP/IP

## Slide 4: 1. Network Hardware
Point-to-point vs broadcast
Networks can be classified by their scale:
Scale | Type
Vicinity | PAN (Personal Area Network) »
Building | LAN (Local Area Network) »
City | MAN (Metropolitan Area Network) »
Country | WAN (Wide Area Network) »
Planet | The Internet (network of all networks)

## Slide 5: Personal Area Network
Connect devices over the range of a person
Example of a Bluetooth (wireless) PAN:

## Slide 6: Local Area Networks
Connect devices in a home or office building
Called enterprise network in a company
Wireless LAN
with 802.11
Wired LAN with
switched Ethernet

## Slide 7: Metropolitan Area Networks
Connect devices over a metropolitan area
Example MAN based on cable TV:

## Slide 8: Wide Area Networks (1)
Connect devices over a country
Example WAN connecting three branch offices:

## Slide 9: Wide Area Networks (2)
An ISP (Internet Service Provider) network is also a WAN.
Customers buy connectivity from the ISP to use it.

## Slide 10: Wide Area Networks (3)
A VPN (Virtual Private Network) is a WAN built from virtual links that run on top of the Internet.

## Slide 11: 2. Network Software/Protocols A. Interfaces/Layers

## Slide 12: What is a protocol?
Formula 1?

## Slide 13: Protocol in Networking
Agreement between communicating parties (peers) on how communication is to proceed
  Peer: processes, devices, humans, …
  Defines
    Syntax: the format of messages
      0-12V, 101001, A-Z, UTF8
    Interaction: the order of messages
    Semantics: meaning of exchanged data and actions to be executed when a message is received

## Slide 14: Protocol Stack
Complexity of networks  layered organization
Standard approach in software engineering
  Separation of duties and responsibilities
  Decomposition
  Decoupling
Layer N
  Offers certain services to layer N+1
  Hides how these services are implemented
  Exploits services made available by layer N-1
Protocol stack: each layer virtually communicates with the corresponding remote layer

## Slide 15: Layers, Protocols, Interfaces
Interface: primitive operations and services made available by a layer to the upper one

## Slide 16: Layers, Protocols, Interfaces
Interface: primitive operations and services made available by a layer to the upper one

## Slide 17: Layers, Protocols, Interfaces
Interface: primitive operations and services made available by a layer to the upper one

## Slide 18: Multilayer Communication
President layer
Secretary Layer
Secret Service Layer
Physical layer
Wir müssen eine gemeinsame Lösung finden
We have to find a common solution
W5t2g0nm4M6yrAgm4azg-9i4gjf40igfa
We have to find a common solution
мы должны найти общее решение

## Slide 19: Example
Service offered by the president layer?
Service offered by the secretary layer?
Interface of the secretary layer?
Service offered by the secret service layer?
Interface of the secret service layer?
Service offered by the physical layer?
Interface of the physical layer?

## Slide 20: Virtual vs actual data flow

## Slide 21: Virtual vs Real Communication
Layer 5: conceptual horizontal communication (send M to …)
Layer 4: header for …?
Layer 3: deals with space limits  message packets
Headers are not seen by layer 5

## Slide 22: Protocol vs Service
Service: operations offered by a layer to the upper one
  Lower layer: service provider (delegation)
  Upper layer: service consumer (abstraction)
  Interface between the two layers
Protocol: governs the interaction between peers, defining the format and meaning of exchanged messages
Service implementation may rely on a protocol (not visible to service consumer)

## Slide 23: Typical protocol components
Addressing
  Many machines, many processes  identification of the recipient of a message
Error control
  Physical communication circuits are not perfect
  Agreement on the control mechanism is needed
  Packets can be out-of-order  reassembling capabilities in the destination
Flow control
  Feedback from receiver to sender
Multiplexing/demultiplexing
  Management of the same connection for multiple conversations
Routing
  Best path for reaching the destination

## Slide 24: Connection(less) Service
Connection-oriented service: creation of a virtual end-to-end communication channel
  Order preservation
  E.g. the telephone system
  Three phases
    Connection establishment and negotiation
    Use of the connection
    Connection release
Connectionless service: fragmentation of interaction into separate messages
  Each message carries the full destination address
  Each message follows a route  possibility of out-of-order messages
  E.g. the postal system

## Slide 25: Quality of Services
The physical layer is inherently unreliable
Implementing reliability above adds complexity
Thus a tradeoff between quality and time

## Slide 26: Service Primitives
Primitives: tell the service to do some action
  Protocol stack in the O.S.  system calls
  Captured by the kernel, which then sends the packets
Primitives depend on the type of service
E.g., primitives for reliable byte stream:

## Slide 27: Service Interaction: Phone Call

## Slide 28: From Abstract to Concrete Models
Abstract model: layered model with services, protocols, interfaces
Concrete model: fixes # layers, content and function of each layer
Two fundamental models
  ISO OSI reference model
    “top-down” (ideal model)
  TCP/IP
    “bottom-up” (widely used protocols)

## Slide 29: 2.B: OSI/ISO Reference Model
Open System Interconnection (1983, revised 1995)
  Targets open systems: systems that are open for communication with other systems
  Interoperability: its goal is to enable cooperation of heterogeneous systems
Well-defined layers
Object-oriented
Abstract model: not bound to specific implementations/vendors

## Slide 30: OSI As a Standard
Driven by ISO (International Organization for Standardization)
With the contribution of
  IEC (International Electrotechnical Commission)
  CCITT (International Telegraph and Telephone Consultative Committee)
  Industrial organizations
    ECMA (European Computer Manufacturers' Association)
    IEEE (Institute of Electrical and Electronics Engineers)
    EIA (Electronic Industries Association)

## Slide 31: OSI Reference Schema
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
Physical Medium
HOST 1
Application
Presentation
Session
Transport
Network
Data link
Physical
HOST 2
A-protocol (APDU)
P-protocol (PPDU)
S-protocol (SPDU)
T-protocol (TPDU)
N-protocol (packet)
D-protocol (frame)
Ph-protocol (bit)
P-Interface
S-interface
T-interface
N-interface
D-interface
Ph-interface

## Slide 32: OSI - Dataflow

## Slide 33: OSI – Interaction Modalities
Connectionless: every SDU managed independently from the others
  No guaranteed QoS
  No memory nor negotiation, just isolated communication
Connection-oriented: connection set up between peers, whose features are negotiated at the beginning
  QoS and support for the three interaction phases
  N.B.: connection maintained by the peers but not necessarily by the intermediate nodes

## Slide 34: OSI - Primitives
7 Layers
3 types of primitives:
  Data: transmission of content
  Connect: opens connection (not used in the connectionless case)
  Disconnect: closes connection (not used in the connectionless case)
4 forms for a primitive:
  Request: (requesting) service user requests a service (action)
  Indication: service provider notifies the (accepting) service user that a service has been requested
  Response: service user provides an answer to a request-for-service
  Confirm: service provider sends back the response related to arequest-for-service
Primitive: <LAYER>-<PRIMITIVE TYPE>.<PRIMITIVE FORM>
  E.g.: Session-connect.response

## Slide 35: OSI – Interaction Patterns
Asynchronous
(no confirm)
(N)-Service User
(N)-Service Provider
(N)-Service User
t
  N-Type.REQUEST
  N-Type.INDICATION
Service not confirmed
Synchronous
Result to client,
with confirm
  N-Type.REQUEST
  N-Type.INDICATION
Service confirmed
  N-Type.RESPONSE
  N-Type.CONFIRM
Blocking asynchrounous
Only confirm
  N-Type.REQUEST
  N-Type.INDICATION
Service partially confirmed
  N-Type.CONFIRM

## Slide 36: OSI Layers 1-2
Physical layer
  Transmission of raw bits over a communication channel
  Decisions on mechanical, electrical, timing issues
  Use of the physical transmission medium below
Data Link
  Transforms a raw transmission facility into a “transmission errors-free” communication line
  Data break up in fragments (~100(0) b) transmitted sequentially

## Slide 37: OSI Layer 3 - Network
Goal: moving messages through the network
  Splits information in packets
Routing strategies and addressing
  Flow control (peers): avoid overload on the reveicer
  Congestion control (network): avoid bottlenecks
  Fairness
node

## Slide 38: OSI Layer 4 - Transport
Receives data from the above, splits it up into smaller units that are then passed to the network layer
Separates the “user/application layers” (above) from the “communication layers” (below)
First layer that virtually connects the two end-points directly
Determines the main features underlying users’ interaction: reliability, ordering of messages, connection(less) interaction,…

## Slide 39: OSI Layer 4 - Transport
Decomposes and reassembles data
  Independently from the network layer
  Multiplexing to recombine the whole info
Analogies from the postal system?

## Slide 40: OSI Layer 4 - Connection
Typical T-interaction modality: connection-oriented
Minimal interaction primitives
  T-CONNECT
    At least source and destination address
    Service with confirmation
  T-DATA
  T-DISCONNECT

## Slide 41: Separation Principle
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
HOST 1
HOST 2
Application
Presentation
Session
Transport
Network
Data link
Physical
Network
Data link
Physical
Network
Data link
Physical
Separation
Interconnection network
user/application protocols

## Slide 42: Why do we not use OSI today?
Too complex
Too late
Too much imposed by government organizations (perceived)

## Slide 43: 2C: Internet and TCP/IP
History of the Internet:
https://www.youtube.com/watch?v=9hIQjrMHTv4
Answer the following question:
  What were the main breakthroughs towards the internet?

## Slide 44: The Internet
A network of networks
Emerged in a bottom-up way
Composed of a set of layers and protocols that became de-facto standards
  TCP/IP
  Not completely aligned with OSI reference model
Born from ARPANET

## Slide 45: Internet Evolution

## Slide 46: Birth of Internet
Late 1950s  USA Department of Defense feared the Cold War
Military communications: public telephone network
  Vulnerable!
Need for a resilient network for military communications

## Slide 47: Baran’s Network
  Paul Baran’s distributed fault-tolerant network
    Based on packet switching
  In the meanwhile, ARPA was created: Advanced Research Projects Agency

## Slide 48: ARPANET
1967: Roberts and Clarks developed a packet-switching
  Cited Baran
  IMP: mini-computers with dynamic routing support

## Slide 49: World-wide Web
Invented by Tim-Berners Lee at CERN in 1989
Distributed open source information space
Documents and other web resources are identified by URLs
Interlinked by hypertext links
Programmed in HTML
Transferred with HTTP
Viewed with browsers
Accessed via the internet

## Slide 50: What is the difference between World Wide Web and Internet?

## Slide 51: TCP/IP
With the growth of ARPANET, it became clear that its protocols were not suited to deal with heterogeneous networks
1974: Cherf and Kahn design TCP/IP
  Specifically tailored to internetworking!
Sockets developed at Berkeley as an API to the network
Rapid growth of ARPANET
  Connection of many LANs
DNS to map logical names to IP addresses
U.S. National Science Foundation creates NSFNET to connect universities
  Connected to ARPANET

## Slide 52: TCP/IP Reference Model
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
OSI
TCP/IP
Application
Transport
Internet
Host-to-network

## Slide 53: TCP/IP Host-to-Network
Usually left almost completely unspecified
Minimal requirement:
  Ability to connect host to network
  Injection of packets
Varies from network to network
We can take the OSI reference model for the physical layer + data link

## Slide 54: Internet Layer (IP)
Connectionless layer supporting
  The injection of packets in any network
  The routing to the destination, possibly across networks
Internet layer like a mail system
Official packet format and transmission protocol: IP (Internet Protocol)
  “Universal” envelope for information

## Slide 55: Transport Layer (TCP/UDP)
Supports conversations between endpoints
Two protocols
  TCP (Transmission Control Protocol)
    Reliable connection-oriented byte stream
    At-most-one semantics
  UDP (User Datagram Protocol)
    Unreliable connectionless protocol
    No sequencing
    May-be semantics

## Slide 56: Application Layer
On top of the transport layer
  Practical experience showed that presentation+session are of little use
Application-level protocols
  Virtual terminal (TELNET)
  File transfer (FTP)
  E-mail (SMTP)
  Naming (DNS)
  World wide web (HTTP)

## Slide 57: OSI vs TCP/IP
Both are multi-layered
OSI: provides a clear separation of services, interfaces, protocols
  Defined “before” protocols
  Far from reality
TCP/IP: sometimes no clear distinction among these three concepts
  Fixed protocols
  Model just describes the existing protocols
   Cannot be used to study e.g. Bluetooth

## Slide 58: Take home (1)
What are services, interfaces and protocols in layered network architectures?
Who invented the internet?
Who invented the world-wide web?
What is the difference between the internet and the WWW?

## Slide 59: Take home (2)
Protocol stack
  Protocols provide services to higher-level protocols
  Interface lower-level protocols
HTTP