## Slide 1: Distributed Systems 4. Data Link Layer
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2015/2016

## Slide 2: The Data Link Layer
Responsible for delivering frames of information over a single link
  Handles transmission errors and regulates the flow of data
Physical
Link
Network
Transport
Application

## Slide 3: The Data Link Layer
  Framing
  Error Detection and Correction
  Elementary Data Link Protocols
  Example Data Link Protocols

## Slide 4: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Actual data path
Virtual data path
Network
Link
Physical

## Slide 5: Possible Services
Unacknowledged connectionless service
  Frame is sent with no connection / error recovery
  Ethernet is example
Acknowledged connectionless service
  Frame is sent with retransmissions if needed
  Example is 802.11 (WiFi)
Connection-oriented service
  Not in this layer

## Slide 6: Why Framing?

## Slide 7: Framing Methods
  Byte count for frames
  Flag bytes with byte stuffing
  Flag bits with bit stuffing
  Physical layer coding violations
    Use non-data symbol to indicate frame

## Slide 8: Framing – Byte count for frames
Frame begins with a count of the number of bytes in it
  Simple, but difficult to resynchronize after an error
Error
case
Expected
case

## Slide 9: Framing – Byte stuffing
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
Stuffing
examples
Frame
format
Need to escape extra ESCAPE bytes too!

## Slide 10: Your turn
What are the frames that were sent?
FLAG A B ESC FLAG C FLAG FLAG ESC ESC ESC FLAG D F ESC FLAG A ESC ESC FLAG FLAG B ESC FLAG D B FLAG

## Slide 11: Framing – Bit stuffing
Stuffing done at the bit level:
  Frame flag has six consecutive 1s (not shown)
  On transmit, after five 1s in the data, a 0 is added
  On receive, a 0 after five 1s is deleted
Transmitted bits
with stuffing
Data bits

## Slide 12: Framing – Physical coding violation
How?

## Slide 13: The Data Link Layer
  Framing
  Error Detection and Correction
  Elementary Data Link Protocols
  Example Data Link Protocols

## Slide 14: Error Detection and Correction
Two basic strategies:
Correct errors at receiver side (using error-correcting codes)
Detect errors at receiver side and request retransmission
Preferred method depends on the error probability
  E.g. fiber: Error detection + retransmission
  E.g. Wifi: Error correcting codes

## Slide 15: FFFooouuunnndddaaatttiiiooonnn ooofff EEErrrrrrooorrr CCCooonnntttttrrrooolll: RRReeeddduuunnndddaaannncccyyy
Dd y knw: Natrl langge cntns a lt f rdndncy. Ths s th rsn tht w cn ndrstnd each otr evn in nsy nvrnmnts
For byte streams without inherent redundancy, we can add redundancy like shown in the title.

## Slide 16: Error Codes
Error codes add structured redundancy to data so errors can be either detected, or corrected.
Error detection codes:
  Parity
  Checksums
  Cyclic redundancy codes (CRC)
Error correction codes:
  Hamming codes
  Reed-Solomon and Low-Density Parity Check codes
    Mathematically complex, widely used in real systems

## Slide 17: Error Detection – Parity
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110 000  1110 0001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 1110 0101; detected, sum is wrong
  Ex: 3 errors, 1101 1001; detected sum is wrong
  Ex: 2 errors, 1110 1101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½

## Slide 18: Error Detection – Checksums
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: IPv4 protocol uses 16-bit checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Detects random errors with probability 1-(1/2)N
  Vulnerable to systematic errors, e.g., added zeros

## Slide 19: Error Detection – CRCs (1)
Adds bits so that transmitted frame viewed as a polynomial is evenly divisible by a generator polynomial
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible

## Slide 20: Error Detection – CRCs (2)
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits (hardware)
Stronger detection than checksums:
  E.g., can detect all double bit errors
  Not vulnerable to systematic errors

## Slide 21: Richard Hamming (1915-1998)
1915-1998
American mathematician
Worked on the Manhattan project
Influence on foundations of communication and networking

## Slide 22: Error Correction – Hamming code
Hamming code gives a simple way to add check bits and correct up to a single bit error:
  Check bits are parity (XOR) over subsets of the codeword
  Recomputing the parity sums (syndrome) gives the position of the error to flip, or 0 if there is no error
  (7,4) Hamming code for (d1,d2,d3,d4,p1,p2,p3)-ordering p1 = d1⊕d2⊕d3 p2 = d2⊕d3⊕d4 p3 = d3⊕d4⊕d1
  Let’s encode 1001 and 0101
p1
d3
p2
p3
d1
d2
d4

## Slide 23
0100 110 1001 110
0001 101 0000 000
0111 010 0110 001
1011 100 0110 001
Decode the following four ASCII characters

## Slide 24: Hamming Codes - Generalization
d data bits
r check bits
Values for d and r that satisfy the following equation allow to correct one error:
d+r+1 ≤ 2r

## Slide 25: Hamming code vs Gray code
??

## Slide 26: Error Detection: IBANs
http://www.ibancalculator.com/
Example:
bank code 123456, bank abbreviation WEST
account number 98765432
Redundancy is in blue
IBAN: |  | GB82 WEST 1234 5698 7654 32 | 
• Rearrange: |  | W E S T12345698765432 G B82 | 
• Convert to integer (A=10, ..) |  | 3214282912345698765432161182 | 
• Compute remainder: |  | 3214282912345698765432161182 | mod 97 = 1

## Slide 27: Error Bounds – Hamming distance
Code turns data of n bits into codewords of n+k bits
Hamming distance is the minimum bit flips to turn one valid codeword into any other valid one.
  Example with 4 codewords of 10 bits (n=2, k=8):
    0000000000, 0000011111, 1111100000, and 1111111111
    Hamming distance is 5
Bounds for a code with distance:
  2d+1 – can correct d errors (e.g., 2 errors above)
  d+1 – can detect d errors (e.g., 4 errors above)

## Slide 28: Error Control - Preference
Which method is better when?
Example:
  Error probability: 10-6
  Frame size: 1k bits
  (7,4)-Hamming code versus one parity bit?

## Slide 29: The Data Link Layer
  Framing
  Error Detection and Correction
  Elementary Data Link Protocols
  Example Data Link Protocols

## Slide 30: Elementary Data Link Protocols
  Link layer environment »
  Utopian Simplex Protocol »
  Stop-and-Wait Protocol for Error-free channel »
  Stop-and-Wait Protocol for Noisy channel »
  Sliding Window concept »

## Slide 31: Link layer environment (1)
Commonly implemented as NICs and OS drivers; network layer (IP) is often OS software

## Slide 32: Link layer environment (2)
Link layer protocol implementations use system calls
Group | Library Function | Description
Network layer | from_network_layer(&packet) to_network_layer(&packet) enable_network_layer() disable_network_layer() | Take a packet from network layer to send Deliver a received packet to network layer Let network cause “ready” events Prevent network “ready” events
Physical layer | from_physical_layer(&frame) to_physical_layer(&frame) | Get an incoming frame from physical layer Pass an outgoing frame to physical layer
Events & timers | wait_for_event(&event) start_timer(seq_nr) stop_timer(seq_nr) start_ack_timer() stop_ack_timer() | Wait for a packet / frame / timer event Start a countdown timer running Stop a countdown timer from running Start the ACK countdown timer Stop the ACK countdown timer

## Slide 33: Utopian Simplex Protocol (=Ethernet)
An optimistic protocol to get us started
  Assumes no errors, and receiver as fast as sender
  Considers one-way data transfer
  That’s it, no error or flow control …
Sender loops blasting frames
Receiver loops eating frames
}

## Slide 34: Stop-and-Wait – Error-free channel
Protocol (p2) ensures sender can’t outpace receiver:
  Receiver returns a dummy frame (ack) when ready
  Only one frame out at a time – called stop-and-wait
  We added flow control!
Sender waits to for ack after passing frame to physical layer
Receiver sends ack after passing frame to network layer

## Slide 35: Stop-and-Wait – Noisy channel (=Wifi)
ARQ (Automatic Repeat reQuest) adds error control
  Receiver acks frames that are correctly delivered
  Sender sets timer and resends frame if no ack
For correctness, frames and acks must be numbered
  Else receiver can’t tell retransmission (due to lost ack or early timer) from new frame
  For stop-and-wait, 2 numbers (1 bit) are sufficient
   Maximum data rate?

## Slide 36: Sliding Window concept (1)
Sender maintains window of frames it has sent
  Needs to buffer them for possible retransmission
  Window advances with next acknowledgements
Receiver maintains window of frames it can receive
  Needs to keep buffer space for arrivals
  Window advances with in-order arrivals

## Slide 37: Sliding Window concept (2)
A sliding window advancing at the sender and receiver
  Ex: window size is 1, with a 3-bit sequence number.

## Slide 38: Sliding Window concept (3)
Larger windows enable pipelining for efficient link use
  Stop-and-wait (w=1) is inefficient for long links
  Best window (w) depends on bandwidth-delay (BD)
  Want w ≥ 2BD to ensure high link utilization
Different choices for errors/buffering
  Go-Back-N: Retransmit all frames since first faulty frame
  Selective Repeat: Retransmit only faulty frames

## Slide 39: The Data Link Layer
  Framing
  Error Detection and Correction
  Elementary Data Link Protocols
  Example Data Link Protocols

## Slide 40: Example Data Link Protocols
  Packet over SONET »
  PPP (Point-to-Point Protocol) »
  ADSL (Asymmetric Digital Subscriber Loop) »

## Slide 41: Packet over SONET/SDH
Packet over SONET is the method used to carry IP packets over SONET optical fiber links (backbone of Internet)
  Uses PPP (Point-to-Point Protocol) for framing
Protocol stacks
PPP frames may be split over SONET payloads

## Slide 42: PPP
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
  Framing uses a flag (0x7E) and byte stuffing
  “Unnumbered mode” (connectionless unacknow-ledged service) is used to carry IP packets
  Errors are detected with a checksum
IP packet
0x21 for IPv4

## Slide 43: ADSL (1)
Widely used for broadband Internet over local loops
  ADSL runs from modem (customer) to DSLAM (ISP)
  IP packets are sent over PPP and AAL5/ATM (over)

## Slide 44: ADSL (2)
PPP data is sent in AAL5 frames over ATM cells:
  ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
  AAL5 is a format to send packets over ATM
  PPP frame is converted to a AAL5 frame (PPPoA)
AAL5 frame is divided into 48 byte pieces, each of which goes into one ATM cell with 5 header bytes

## Slide 45: Take home
Why framing is needed and how it can be done with byte stuffing
Error detection + retransmission versus error correction
(7,4)-Hamming code
Acknowledgements with sliding windows
Next
  Lecture: Some link layer exercises
  Real lecture: How to share a link (Medium access control sublayer)
  Real lab: Experimenting with a simple link layer protocol simulation