## Slide 1: Distributed Systems 7. Medium Access Control Sublayer
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2015/2016

## Slide 2: The MAC Sublayer
Responsible for deciding who sends next on a multi-access link
  An important part of the link layer, especially for LANs
Physical
Link
Network
Transport
Application
MAC is in here!

## Slide 3: Medium Access Control Sublayer
  Channel Allocation Theory
  Ethernet
  Wireless Channel Allocation
  WiFi
  Data Link Layer Switching

## Slide 4: Medium Access Control Sublayer
  Channel Allocation Theory
  Ethernet
  Wireless Channel Allocation
  WiFi
  Data Link Layer Switching

## Slide 5: Static Channel Allocation
For fixed channel and traffic from N users
  Divide up bandwidth using FDM or TDM
  Example: FM radio
Why not a good idea for LANs?

## Slide 6: Multiple Access Protocols
  Dynamic allocation gives the channel to a user when they need it. Potentially N times as efficient for N users.
  Contention protocols
    ALOHA
    CSMA (Carrier Sense Multiple Access)
  Collision-free protocols
    Token ring
    Bitmap
  Limited-contention protocols
    Adaptive treewalk
  Wireless LAN protocols

## Slide 7
ALOHA

## Slide 8: ALOHA (1)
In pure ALOHA, users transmit frames whenever they have data; users retry after a random time for collisions
  Efficient and low-delay under low load
`
Collision
Collision
Time
User
A
B
C
D
E

## Slide 9: ALOHA (2)
Collisions happen when other users transmit during a vulnerable period that is twice the frame time
  Synchronizing senders to slots can reduce collisions

## Slide 10: ALOHA (3)
Slotted ALOHA is twice as efficient as pure ALOHA
  Low load wastes slots, high loads causes collisions
  Efficiency up to 1/e (37%) for random traffic models

## Slide 11: CSMA (1)
CSMA improves on ALOHA by sensing the channel
  User doesn’t send if it senses someone else
Variations on what to do if the channel is busy:
  1-persistent (greedy) sends as soon as idle
  Nonpersistent waits a random time then tries again
  p-persistent sends with probability p when idle (slotted)

## Slide 12: CSMA (2) – Persistence
CSMA outperforms ALOHA, and being less persistent is better under high load

## Slide 13: CSMA (3) – Collision Detection
CSMA/CD improvement is to detect/abort collisions
  Reduced contention times improve performance
Collision time is much shorter than frame time

## Slide 14: CSMA/CD
http://scisweb.ulster.ac.uk/~kevin/com320/labs/Simulations/csmacd.swf

## Slide 15: Collision-Free – Token Ring
A Kwakwaka'wakw man with a talking stick (Source: Wikipedia)

## Slide 16: Collision-Free – Token Ring
Token sent round ring defines the sending order
  Station with token may send a frame before passing
  Idea can be used without ring too, e.g., token bus
Station
Direction of
transmission
Token

## Slide 17: Collision-Free – Bitmap
Optimization to reduce impact of empty slots
The basic bit-map protocol:
  Sender set a bit in contention slot if they have data
  Senders send in turn; everyone knows who has data
Problems?

## Slide 18: Contention vs. Contention-free protocols
10 participants: CSMA versus Token Ring
Chart: G (attempts per packet time)
Y-Values
Ideal

## Slide 19: Contention vs collision-free protocols
Contention protocols good for low load, but bad for high load.
Collision-free ones bad for low load, acceptable for high load
  Still, if load is very high, static schemes may be better, due to unnecessary sending order resolution (if everybody wants to send anyway)
Can we combine contention and collision-free protocols?

## Slide 20
Blood samples from 1000 soldiers
One of them is sick.
How many samples need to be checked to find that soldier?

## Slide 21: Limited Contention – Adaptive Tree Walk
Tree divides stations into groups (nodes) to poll
  Depth first search under nodes with poll collisions
  Start search at lower levels if >1 station expected
Level 0
Level 1
Level 2
What happens when A, C and G want to send?

## Slide 22: Your turn
16 stations, of which all prime numbers want to send.
What happens on the channel?

## Slide 23: Medium Access Control Sublayer
  Channel Allocation Theory
  Ethernet
  Wireless Channel Allocation
  WiFi
  Data Link Layer Switching

## Slide 24: MAC-Adresses
Typically hardcoded by the manufacturer
Ipconfig /all
IEEE manages three spaces: MAC-48, EUI-48, and EUI-64
Great for spying

## Slide 25: Classic Ethernet (1) – Physical Layer
One shared coaxial cable to which all hosts attached
  10 Mbps: Manchester encoding
  100 Mbps: 4B/5B encoding
  1000 Mbps: 8B/10B encoding
  Hosts run the classic Ethernet CSMA/CD protocol for access
Hub

## Slide 26: Classic Ethernet (2) – MAC
MAC protocol waits randomly longer in case of repeated collisions
  Random delay (backoff) after collision is computed with BEB (Binary Exponential Backoff)
   After first collision, wait between 0 and 1 time units, after second, between 0 and 3, after third, between 0 and 7, …
IEEE 802.3
Problem: Frame length – bandwidth – round-trip-time tradeoff

## Slide 27: Classic Ethernet (4) – Performance
Efficient for large frames, even with many senders
  Degrades for small frames (and long LANs)
10 Mbps Ethernet,
64 byte min. frame

## Slide 28: Medium Access Control Sublayer
  Channel Allocation Theory
  Ethernet
  Wireless Channel Allocation
  WiFi
  Data Link Layer Switching

## Slide 29: Wireless LAN Protocols (1)
Wireless has complications compared to wired.
Nodes may have different coverage regions
  Leads to problems with hidden and exposed terminals
Nodes can’t detect all collisions, i.e., sense while sending
  Makes collisions expensive and to be avoided

## Slide 30: Wireless LANs (2) – Hidden terminals
Hidden terminals are senders that cannot sense each other but nonetheless collide at intended receiver
  Want to prevent; loss of efficiency
  A and C are hidden terminals when sending to B

## Slide 31: Wireless LANs (3) – Exposed terminals
Exposed terminals are senders who can sense each other but still transmit safely (to different receivers)
  Desirably concurrency; improves performance
  B  A and C  D are exposed terminals

## Slide 32: Wireless LANs (4) – MACA
MACA protocol grants access for A to send to B:
  A sends RTS to B [left]; B replies with CTS [right]
  A can send with exposed but no hidden terminals
  A sends RTS to B; C and E hear and defer for CTS
  B replies with CTS; D and E hear and defer for data

## Slide 33: Medium Access Control Sublayer
  Channel Allocation Theory
  Ethernet
  Wireless Channel Allocation
  WiFi
  Data Link Layer Switching

## Slide 34: Wireless LANs
  802.11 physical layer
  802.11 MAC
  802.11 frames

## Slide 35: 802.11 Architecture/Protocol Stack (1)
Wireless clients associate to a wired AP (Access Point)
  Called infrastructure mode; there is also ad-hoc mode with no AP, but that is rare.
Access Point
Client
To Network

## Slide 36: 802.11 physical layer
  NICs are compatible with multiple physical layers
    E.g., 802.11 a/b/g
Name | Technique | Max. Bit Rate
802.11b | Spread spectrum, 2.4 GHz | 11 Mbps
802.11g | OFDM, 2.4 GHz | 54 Mbps
802.11a | OFDM, 5 GHz | 54 Mbps
802.11n | OFDM with MIMO, 2.4/5 GHz | 600 Mbps

## Slide 37: 802.11 MAC
Base station mode: Base station pulls, no collisions
Ad-hoc mode: CSMA/CD with RTS/CTS
NAV = channel not available

## Slide 38: 802.11 MAC (2)
  Different backoff slot times add quality of service
    Short intervals give preferred access, e.g., control, VoIP

## Slide 39: 802.11 Frames
  Frames vary depending on their type (Frame control)
  Data frames have 3 addresses to pass via APs

## Slide 40: Medium Access Control Sublayer
  Channel Allocation Theory
  Ethernet
  Wireless Channel Allocation
  WiFi
  Data Link Layer Switching

## Slide 41: Data Link Layer Switching
  How to set up large Ethernets?
    Hubs
    Switches
    Routers (are part of the Network layer)

## Slide 42: Switched/Fast Ethernet (1)
  Hubs wire all lines into a single CSMA/CD domain
  Switches isolate each port to a separate domain
    Much greater throughput for multiple ports
    No need for CSMA/CD with full-duplex lines

## Slide 43: Uses of Switches
Common setup is a building with centralized wiring
  Switches are placed in or near wiring closets

## Slide 44: Learning Switches (2)
Backward learning algorithm picks the output port:
  Associates source address on frame with input port
  Frame with destination address sent to learned port
  Unlearned destinations are sent to all other ports
Needs no configuration
  Forget unused addresses to allow changes
  Bandwidth efficient for two-way traffic
Switch

## Slide 45: Take home
Protocols for multiple access
  Contention protocols: ALOHA, CSMA/CD
  Contention-free protocols: Token ring, Bitmap
  Mixed protocols: Adaptive tree walk
Practically used techniques
  Ethernet/WiFi: CSMA/CD with random exponential backoff
Link Layer switching:
  Hubs vs. Switches
Next: Network Layer

## Slide 46: Bonus: RFID

## Slide 47: RFID
  Gen 2 Architecture »
  Gen 2 Physical Layer »
  Gen 2 Tag Identification Layer »
  Gen 2 Frames »

## Slide 48: RFID Gen 2 Architecture
Reader signal powers tags; tags reply with backscatter

## Slide 49: RFID Gen 2 Physical Layer
  Reader uses duration of on period to send 0/1
  Tag backscatters reader signal in pulses to send 0/1

## Slide 50: RFID Gen 2 Tag Identification Layer
Reader sends query and sets slot structure
Tags reply (RN16) in a random slot; may collide
Reader asks one tag for its identifier (ACK)
Process continues until no tags are left

## Slide 51: Gen 2 Frames
  Reader frames vary depending on type (Command)
    Query shown below, has parameters and error detection
  Tag responses are simply data
    Reader sets timing and knows the expected format
Query message