## Slide 1: Distributed Systems 10. Network Layer in the Internet
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2015/2016

## Slide 2: The Network Layer
Remember:
Responsible for delivering packets between endpoints over multiple links
(Link layer: single link Transport layer: Uses this service)
Physical
Link
Network
Transport
Application

## Slide 3: Network Layer in the Internet (1)
  IP Version 4
  IP Addresses
  IP Version 6
  Internet Control Protocols
  Label Switching and MPLS
  OSPF—An Interior Gateway Routing Protocol
  BGP—The Exterior Gateway Routing Protocol
  Mobile IP

## Slide 4: Network Layer in the Internet (3)
Internet is an interconnected collection of many networks that is held together by the IP protocol

## Slide 5: IP Version 4 Protocol (1)
IPv4 (Internet Protocol) header is carried on all packets and has fields for the key parts of the protocol:

## Slide 6: Wireshark

## Slide 7: Hierarchical Routing – Classful Addresing
Old addresses came in blocks of fixed size (A, B, C)
  Carries size as part of address, but lacks flexibility
  Called classful (vs. classless) addressing
   Router need only one entry per external subnet

## Slide 8: IP Addresses (1) – Prefixes
Addresses are allocated in blocks called prefixes
  Prefix is determined by the network portion
  Written address/length, e.g., 18.0.31.0/24

## Slide 9: IP Addresses (2) – Subnets
Subnetting splits up IP prefix to help with management
  Looks like a single prefix outside the network
Network divides it into subnets internally
ISP gives network
a single prefix

## Slide 10: Your turn
Subnet A has address 141.89.228.0/26
How many addresses are in this subnet?
What is the lowest, what is the highest address in this subnet?
Computer B has the IPv4 address (including the subnet mask in CIDR notation) 141.89.228.65/26.
Computer C is reachable as 141.89.228.63/26.
Do they belong to the same subnet?

## Slide 11: IP Addresses (3) – Aggregation
Aggregation joins multiple IP prefixes into a single larger prefix to reduce routing table size
 Reduce size of the routing table
ISP customers have different prefixes
ISP advertises
a single prefix

## Slide 12: Your turn (2)
Split the subnet 192.168.240.0/12 into four equal subnets and give the address of each subnet

## Slide 13: IP Addresses (4) – Longest Matching Prefix
Packets are forwarded to the entry with the longest matching prefix or smallest address block
  Complicates forwarding but adds flexibility
Main prefix goes this way
Except for this part!

## Slide 14: IP Version 6 (1)
Major upgrade in the 1990s due to impending address exhaustion, with various other goals:
    Support billions of hosts
    Reduce routing table size
    Simplify protocol
    Better security
    Attention to type of service
    Aid multicasting
    Roaming host without changing address
    Allow future protocol evolution
    Permit coexistence of old, new protocols, …
Deployment has been slow & painful, but may pick up pace now that addresses are all but exhausted

## Slide 15: How many addresses?
Three hundred and forty undecillion, two hundred and eighty-two decillion, three hundred and sixty-six nonillion, nine hundred and twenty octillion, nine hundred and thirty-eight septillion, four hundred and sixty-three sextillion, four hundred and sixty-three quintillion, three hundred and seventy-four quadrillion, six hundred and seven trillion, four hundred and thirty-one billion, seven hundred and sixty-eight million, two hundred and eleven thousand, four hundred and fifty-six.

## Slide 16: IP Version 6 (2 )
IPv6 protocol header has much longer addresses (128 vs. 32 bits) and is simpler (by using extension headers)

## Slide 17: IP Version 6 (3)
IPv6 extension headers handles other functionality

## Slide 18: IPv6 Deployment Status
https://www.vyncke.org/ipv6status/
http://test-ipv6.com/

## Slide 19: Internet Control Protocols (1)
IP works with the help of several control protocols:
  ICMP is a companion to IP that returns error info
    Required, and used in many ways, e.g., for traceroute
  ARP finds Ethernet address of a local IP address
    Glue that is needed to send any IP packets
    Host queries an address and the owner replies
  DHCP assigns a local IP address to a host
    Gets host started by automatically configuring it
    Host sends request to server, which grants a lease

## Slide 20: Internet Control Protocols (2)
Main ICMP (Internet Control Message Protocol) types:

## Slide 21: Internet Control Protocols (3)
ARP (Address Resolution Protocol) lets nodes find target Ethernet addresses [pink] from their IP addresses
Broadcast: “Who has IP X?”
Router takes all external addresses

## Slide 22: Label Switching and MPLS (1)
MPLS (Multi-Protocol Label Switching) sends packets along established paths; ISPs can use for QoS
  Path indicated with label below the IP layer

## Slide 23: Label Switching and MPLS (2)
Label added based on IP address on entering an MPLS network (e.g., ISP) and removed when leaving it
  Forwarding only uses label inside MPLS network

## Slide 24: OSPF— Interior Routing Protocol
OSPF computes routes for a single network (e.g., ISP)
  Models network as a graph of weighted edges
Network:
Graph:
Broadcast LAN modeled as a well-connected node
3

## Slide 25: OSPF— Interior Routing Protocol (3)
OSPF (Open Shortest Path First) is link-state routing:
  Uses messages below to reliably flood topology
  Then runs Dijkstra to compute routes

## Slide 26: BGP— Exterior Routing Protocol (1)
BGP (Border Gateway Protocol) computes routes across interconnected, autonomous networks
  Key role is to respect networks’ policy constraints
Example policy constraints:
    No commercial traffic for educational network
    Never put Iraq on route starting at Pentagon
    Choose cheaper network
    Choose better performing network
    Don’t go from Apple to Google to Apple

## Slide 27: BGP— Exterior Routing Protocol (2)
Common policy distinction is transit vs. peering:
  Transit carries traffic for pay; peers for mutual benefit
  AS1 carries AS2↔AS4 (Transit) but not AS3 (Peer)

## Slide 28: BGP— Exterior Routing Protocol (3)
BGP propagates messages along policy-compliant routes
  Message has prefix, AS path (to detect loops) and next-hop IP (to send over the local network)

## Slide 29: Mobile IP
Mobile hosts can be reached at fixed IP via a home agent
  Home agent tunnels packets to reach the mobile host; reply can optimize path for subsequent packets
  No changes to routers or fixed hosts

## Slide 30: Take home
Internet Protocol (IP)
  NETID+HOSTID
  Subnetting
Internet
  MPLS for sending along defined paths
  OSPF inside a network
  BGP between networks
IP Simulation: http://www.cs.stir.ac.uk/~kjt/software/comms/jasper/IP.html