## Slide 1: Distributed Systems 3. Physical Layer
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2016/2017
Notes: Interaktiv:
frequencies per signal rate – berechnen
bandwidth of a truck berechnen
(gray code)

## Slide 2: The Physical Layer
  Theoretical Basis for Data Communications
  Transmission Media
    Guided Transmission Media
    Wireless Transmission
    Communication Satellites
  Digital Modulation and Multiplexing
  Example Networks
    Public Switched Telephone Network
    Mobile Telephone System

## Slide 3: The Physical Layer
Foundation on which other layers build
  Properties of wires, fiber, wireless limit what the network can do
Key problem is to send (digital) bits using only (analog) signals
  This is called modulation
Physical
Link
Network
Transport
Application

## Slide 4: The Physical Layer
  Theoretical Basis for Data Communications
  Transmission Media
    Guided Transmission Media
    Wireless Transmission
    Communication Satellites
  Digital Modulation and Multiplexing
  Example Networks
    Public Switched Telephone Network
    Mobile Telephone System

## Slide 5: What limits communication?
Examples:
Light
Sound

## Slide 6: Electromagnetic signals
Limiting factor 1: Bandwidth:
Maximum frequency that can be transmitted and decoded over a medium
Limited either due to:
  Physical properties of the medium (e.g. attenuation for electrical signals)
  Physical limits of the encoder/decoder
Measured in Hertz (1 Hz = 1/s)
Notes: TV channel 6 Mhz
Wifi 20 Mhz
DSL 1 Mhz

## Slide 7: Fourier Analysis
A time-varying signal can be equivalently represented as a series of frequency components (harmonics):
a, b weights of harmonics
Signal over time
=
Notes: rms = root mean square

## Slide 8: Visualization
http://www.intmath.com/fourier-series/fourier-graph-applet.php

## Slide 9: Bandwidth-Limited Signals
Having less bandwidth (harmonics) degrades the signal
8 harmonics
4 harmonics
2 harmonics
Lost!
Bandwidth
Lost!
Lost!
Notes: bandwidth = max frequency transmittable

## Slide 10: Maximum Data Rate of a Channel
Nyquist’s theorem (1924) relates the data rate to the bandwidth (B) and limiting factor 2, the number of signal levels (V):
Maximum data rate of a binary signal over a 3kHz channel is 6Kbps
Shannon’s result relates data rate to bandwidth (B) and the signal-to-noise (S/N) ratio
 Maximum data rate of over a 1 MHz DSL-line with signal-to-noise ratio 10000:1 (40 db) is 13 Mbps
Max. data rate = 2B log2V bits/sec
How fast signal
can change
How many levels
can be seen
Max. data rate = B log2(1+S/N)
Notes: These are fundamental limits; real systems can only approach them.
Formula 1: Modem 56k modem same channel -> 512 levels
Formula 1: Wifi: 20 Mhz -> 40 Mbit/s
Formula 2: Wifi: 20 Mhz, SNR 1000 (30 db) -> 200 Mbit/s

## Slide 11
Notes: Canada goose, not grey
Closed 2013
Florham park, NJ

## Slide 12: The Physical Layer
  Theoretical Basis for Data Communications
  Transmission Media
    Guided Transmission Media
    Wireless Transmission
    Communication Satellites
  Digital Modulation and Multiplexing
  Example Networks
    Public Switched Telephone Network
    Mobile Telephone System

## Slide 13: Wires – Twisted Pair
Very common; used in LANs, telephone lines
  Twists reduce radiated signal (interference)
Category 5 UTP cable with four twisted pairs
Notes: signal as diff between the two cables -> external noise affects both the same
phones to telco for some kilometers use this
several mbit/sec for few kilometers
CAT5 four such pairs
100 mbit lan uses two of them, one each direction
1gb lan uses all four both directions

## Slide 14: Wires – Coaxial Cable (“Co-ax”)
Also common. Better shielding and more bandwidth for longer distances and higher rates than twisted pair.
Notes: coax: few Ghz
old time: long distance phone, now replaced by fiber
for TV a lot
More expensive

## Slide 15: Wires – Power Lines
Household electrical wiring is another example of wires
  Convenient to use, but horrible for sending data
Notes: It is horrible because it carries power signals at the same time and the wiring was not designed for data communications, e.g., it is not tightly twisted like twisted pair, and its electrical properties change as devices that are plugged in turn on and off. But it is convenient because it is already installed and many devices are plugged in to get power, so people are starting to use it.
In germany, internet offered that way some time
In italy, responders for electric counting can be switched on and of with this

## Slide 16: Fiber Cables (1)
Common for high rates and long distances
  Long distance ISP links, Fiber-to-the-Home
  Light carried in very long, thin strand of glass
Light source
(LED, laser)
Photodetector
Light trapped by
total internal reflection
Notes: optical fiber. It is widely used for links that run at high rates, particularly over long distances. The optical fiber is a very long, thin strand of glass. Either a LED or a laser (better quality, more expensive). The pulses of light are trapped in the fiber (total internal reflection) and follow it. At the other end a photodetector turns pulses of light into electrical signals.

## Slide 17: Fiber Cables (2)
Fiber has enormous bandwidth (THz) and tiny signal loss – hence high rates over long distances
3 dB = half point of energy
Notes: This slide shows why fiber runs for high rates and long distances – attenuation is very low (can go 10km before the signal has lost 3dB or half its power) for enormous regions of bandwidth (30 *Terahertz* when wavelength is converted to frequency).

## Slide 18: Fiber Cables (3)
Comparison of the properties of wires and fiber:
Property | Wires | Fiber
Distance | Short (100s of m) | Long (tens of km)
Bandwidth | Moderate | Very High
Cost | Inexpensive | Less cheap
Convenience | Easy to use | Less easy
Security | Easy to tap | Hard to tap
Notes: Fiber gives you very high rates over long runs; wires score less highly on these properties and support high rates over much shorter runs. But wires are usually the inexpensive solution when the transmission/reception hardware is included. Wires are also easier to work with; fiber requires greater care with connections. Fiber has the advantage that it is very hard to tap as the light is confined only to the fiber or the fiber is broken. Wires are usually easy to tap because they radiate the signal well.

## Slide 19: Wireless Transmission
  Electromagnetic Spectrum »
  Radio Transmission »
  Microwave Transmission »
  Light Transmission »
  Wireless vs. Wires/Fiber »

## Slide 20: Electromagnetic Spectrum (1)
Different bands have different uses:
    Radio: wide-area broadcast; Infrared/Light: line-of-sight
    Microwave: LANs and 3G/4G;
Microwave
Networking focus

## Slide 21: Electromagnetic Spectrum (3)
Fortunately, there are unlicensed (“ISM”) bands:
    Free for use at low power; devices manage interference
    Widely used for networking; WiFi, Bluetooth, etc.
802.11
b/g/n
802.11a/g/n
Notes: These bands are used for WiFi, etc., not for cellular.

## Slide 22: Electromagnetic Spectrum (2)
To manage interference, spectrum is carefully divided, and its use regulated and licensed, e.g., sold at auction.
Source: NTIA Office of Spectrum Management, 2003
3 GHz
30 GHz
3 GHz
300 MHz
WiFi (ISM bands)
(Excerpt of the US frequency allocations)
Notes: TV, cellular, satellite frequencies are heavily regulated.

## Slide 23: Radio Transmission
In the HF band, radio waves bounce off the ionosphere.
In the VLF, LF, and MF bands, radio waves follow the curvature of the earth
Radio signals penetrate buildings well and propagate for long distances with path loss
Notes: The path loss makes the signal fall of at least as fast as 1/d^2 due to the RF energy being spread out over a greater region.

## Slide 24: Microwave Transmission
Microwaves have much bandwidth and are widely used indoors (WiFi) and outdoors (3G, satellites)
  Signal is attenuated/reflected by everyday objects
  Strength varies due multipath fading, etc.
Notes: The variation in signal strength as the sender/receiver move is a key hallmark of wireless. It means that data rates over wireless links can change dramatically; they are not fixed like a wire.
Routing around rain, reflections cancel out stuff, water absorbs them

## Slide 25
Source: http://www.howtogeek.com/171869/why-does-running-my-microwave-kill-my-wi-fi-connectivity/

## Slide 26: Wireless vs. Wires/Fiber
Wireless:
    Easy and inexpensive to deploy
    Naturally supports mobility
    Naturally supports broadcast
    Transmissions interfere and must be managed
    Signal strengths hence data rates vary greatly
Wires/Fiber:
    Easy to engineer a fixed data rate over point-to-point links
    Can be expensive to deploy, esp. over distances
    Doesn’t readily support mobility or broadcast

## Slide 27: Communication Satellites
Satellites are effective for broadcast distribution and anywhere/anytime communications
  Kinds of Satellites »
  Geostationary (GEO) Satellites »
  Low-Earth Orbit (LEO) Satellites »
  Satellites vs. Fiber »

## Slide 28: Kinds of Satellites
Satellites and their properties vary by altitude:
  Geostationary (GEO), Medium-Earth Orbit (MEO), and Low-Earth Orbit (LEO)
Sats needed for global coverage
GPS, Galileo
Notes: MEO is used for navigation systems such as the GPS (Global Positioning System) rather than data communications.

## Slide 29: Geostationary Satellites
GEO satellites orbit 35,000 km above a fixed location
    VSAT (computers) can communicate with the help of a hub
    Different bands (L, S, C, Ku, Ka) in the GHz are in use but may be crowded or susceptible to rain.
VSAT
GEO satellite
Notes: very small aperture antennas (1m only)

## Slide 30: Low-Earth Orbit Satellites
Systems such as Iridium (satellite phones) use many low-latency satellites for coverage and route communications via them
The Iridium satellites form six necklaces around the earth.
Notes: Since the satellites are LEO, it does not take long for signals from the Earth to go up and down compared to GEO satellites.
A bit outdated now, with mobile network coverage on ground good

## Slide 31: Satellite vs. Fiber
Satellite:
    Can rapidly set up anywhere/anytime communications (after satellites have been launched)
    Can broadcast to large regions
    Limited bandwidth and interference to manage
Fiber:
    Enormous bandwidth over long distances
    Installation can be more expensive/difficult

## Slide 32: Bandwidth
Internal/Home Network
Internet link
Connection | Speed |  | Transmit 1 GB
type | bps | B/sec | hh : mm : ss
56K Modem | 56 K | 6.8 K | 42 : 36 : 31.69
Classic DSL | 512 K | 62.5 K | 4 : 39 : 37.22
Modern DSL | 10 M | 1.221 M | : 14 : 09.93
OC-1 | 51.840 M | 6.328 M | : 2 : 45.70
Ethernet | 100 M | 12.207 M | : 1 : 25.90
OC-3 | 155 M | 18.984 M | : : 55.23
OC-12 | 622 M | 75.937 M | : : 13.81
Notes: optical carrier

## Slide 33: The best bandwidth in the world?
What if we send a truck forth and back?
7.1PB of storage (http://searchdatacenter.techtarget.com/review/Rackable-Systems-ICE-Cube-Modular-Data-Center)
transmission speed: 80 km/h
Bandwidth Rome-London (2000 km)?
Notes: 78 GB/s vs 75 GB/s
Send it forth and back and forth and back

## Slide 34: The Physical Layer
  Theoretical Basis for Data Communications
  Transmission Media
    Guided Transmission Media
    Wireless Transmission
    Communication Satellites
  Digital Modulation and Multiplexing
  Example Networks
    Public Switched Telephone Network
    Mobile Telephone System

## Slide 35: Digital Modulation
Modulation schemes send bits as signals;
Single-dimension modulation (Baseband Transmission)
Multi-dimension modulation (Passband Transmission)

## Slide 36: Baseband Transmission
Line codes send symbols that represent one or more bits
  NRZ is the simplest, literal line code (+1V=“1”, -1V=“0”)

## Slide 37: Baseband transmission (2)
To decode the symbols, signals need sufficient transitions
  Otherwise long runs of 0s (or 1s) are confusing, e.g.:
Strategies:
  Manchester coding, mixes clock signal in every symbol
  4B/5B maps 4 data bits to 5 coded bits with 1s and 0s:
  Scrambler XORs tx/rx data with pseudorandom bits
1
0 0 0 0 0 0 0 0 0 0 um, 0? er, 0?
Data | Code | Data | Code | Data | Code | Data | Code
0000 | 11110 | 0100 | 01010 | 1000 | 10010 | 1100 | 11010
0001 | 01001 | 0101 | 01011 | 1001 | 10011 | 1101 | 11011
0010 | 10100 | 0110 | 01110 | 1010 | 10110 | 1110 | 11100
0011 | 10101 | 0111 | 01111 | 1011 | 10111 | 1111 | 11101
Notes: Strategies go from simplest to more complex and make progressively better use of bandwidth:
-Manchester is simple (every symbol has an embedded transition) but uses twice the bandwidth of a data signal
-4B/5B ensures no more than three 0s in a row (1s can be handled by making the signal level change to represent a 1) and needs 1.25X bandwidth
-scrambler needs no extra bandwidth (just data XOR sequence XOR sequence = data) but only makes long runs of 0s or 1s a low probability event

## Slide 38: Passband Transmission (1)
Modulating the amplitude, frequency/phase of a carrier signal sends bits in a (non-zero) frequency range
NRZ signal of bits
Amplitude shift keying
Frequency shift keying
Phase shift keying
Notes: nyquist says there is no point in sampling higher than 6000 times per second for binary signal over 3khz line
therefore, increase signal from binary to more

## Slide 39: Passband Transmission (2)
BPSK
2 symbols
1 bit/symbol
QPSK
4 symbols
2 bits/symbol
QAM-16
16 symbols
4 bits/symbol
QAM-64
64 symbols
6 bits/symbol
QAM varies amplitude and phase
BPSK/QPSK varies only phase
Constellation diagrams are a shorthand to capture the amplitude and phase modulations of symbols:
Notes: binary phase shift keying, quadrature amplitude modification
1. up/down
2. three different phasenverschiebungen
QAM: phase + amplitude + phase
3. => 4 bits per symbol
highest: 14bits/symbol => 33kb (+compression etc)

## Slide 40: Twodimensional case – Gray coding
2 dimensions with four levels each
A
B
C
D
E

## Slide 41: Gray code exercise
3 bit in a signal ranging from 0-8V
0-1V: 000
1-2V: 001
2-3V: 010
3-4V: 011
4-5V: 100
5-6V: 101
6-7V: 110
7-8V: 111
Why is this arrangement not good?
What would be a better one?

## Slide 42: Multiplexing
  Multiplexing schemes share a channel among users.
  Frequency Division Multiplexing
  Time Division Multiplexing
Will see dynamic schemes in the medium access control sublayer

## Slide 43: Frequency Division Multiplexing (1)
FDM (Frequency Division Multiplexing) shares the channel by placing users on different frequencies:
Overall FDM channel

## Slide 44: Time Division Multiplexing (TDM)
Time division multiplexing shares a channel over time:
  Users take turns on a fixed schedule; this is not packet switching or STDM (Statistical TDM)
  Widely used in telephone / cellular systems

## Slide 45: The Physical Layer
  Theoretical Basis for Data Communications
  Transmission Media
    Guided Transmission Media
    Wireless Transmission
    Communication Satellites
  Digital Modulation and Multiplexing
  Example Networks
    Public Switched Telephone Network
    Mobile Telephone System

## Slide 46: The Public Switched Telephone Network
  Structure of the telephone system »
  Politics of telephones »
  Local loop: modems, ADSL, and FTTH »
  Trunks and multiplexing »
  Switching »

## Slide 47: Structure of the Telephone System
A hierarchical system for carrying voice calls made of:
  Local loops, mostly analog twisted pairs to houses
  Trunks, digital fiber optic links that carry calls
  Switching offices, that move calls among trunks

## Slide 48: Local loop (1): modems
Telephone modems send digital data over an 3.3 KHz analog voice channel interface to the plain old phone network
  Rates <56 kbps; early way to connect to the Internet

## Slide 49: Local loop (2): Digital Subscriber Lines
DSL broadband sends data over the local loop to the local office using frequencies that are not used for POTS
  Telephone/computers attach to the same old phone line
  Rates vary with line
  OFDM is used up to 1.1 MHz for ADSL2
    Most bandwidth down
Notes: ADSL for “asymmetric DSL” is the most popular version of DSL. Asymmetric cause more for down.
Orthogonal frequency-division multiplexing
Pay for getting filter removed…

## Slide 50: Switching (1)
PSTN uses circuit switching; Internet uses packet switching
Notes: public switched telephone network
Pro: only limit by speed of electricity
Pro: no congestion
Con: more expensive, less fault-proof

## Slide 52: Strowger Switches (1891)
Notes: Story: undertaker – 2 in missouri, manual connection, other one’s wife was operator => invented automatic switching

## Slide 53: Switching (2)
Circuit switching requires call setup (connection) before data flows smoothly
  Also teardown at end (not shown)
Packet switching treats messages independently
  No setup, but variable queuing delay at routers
Circuits
Packets

## Slide 54: Switching (3)
Comparison of circuit- and packet-switched networks

## Slide 55: Mobile Telephone System
  Generations of mobile telephone systems »
  Cellular mobile telephone systems »
  GSM, a 2G system »
  UMTS, a 3G system »

## Slide 56: Generations of mobile telephone systems
1G, analog voice
    AMPS (Advanced Mobile Phone System) is example, deployed from 1980s. Modulation based on FM (as in radio).
2G, analog voice and digital data
    GSM (Global System for Mobile communications) is example, deployed from 1990s. Modulation based on QPSK.
    First SIM cards 1991
3G, digital voice and data
    UMTS (Universal Mobile Telecommunications System) is example, deployed from 2000s. Modulation based on CDMA
    Frequency auctions: 200 €/inhabitant in Italy
4G, digital data including voice
    LTE (Long Term Evolution) is example, deployed from 2010s. Modulation based on OFDM
Notes: FM = freq division
QPSK = Quadrature Phase Shift Keying (QPSK)
CDMA = code division multiple access – overlay with different bytecodes parts…
OFDM = FDM on different subchannels, better for variable channels, when high end unreliable

## Slide 57: Cellular mobile phone systems
All based on notion of spatial regions called cells
    Each mobile uses a frequency in a cell; moves cause handoff
    Frequencies are reused across non-adjacent cells
Cellular reuse pattern
Smaller cells for dense mobiles
Notes: General Packet Radio Service
Gateway GPRS support node (GGSN)
Serving GPRS support node (SGSN)

## Slide 58: GSM – Global System for Mobile Communications (1)
  Mobile is divided into handset and SIM card (Subscriber Identity Module) with credentials
    IMSI (International Mobile Subscriber Identity
    Authentication information
  Mobiles tell their HLR (Home Location Register) their current whereabouts for incoming calls
  Cells keep track of visiting mobiles (in the Visitor LR)
Notes: Mobile switching center
Base station controller

## Slide 59: GSM – Global System for Mobile Communications (2)
Air interface is based on FDM channels of 200 KHz divided in an eight-slot TDM frame every 4.615 ms
  Mobile is assigned up- and down-stream slots to use
  Each slot is 148 bits long, gives rate of 27.4 kbps
Notes: GSM runs mostly in 850 / 900 / 1800 / 1900 MHz spectrum depending on the country
Frequency division multiplexing, time division multiplexing
27.4 kbps is best case…

## Slide 60: UMTS – Universal Mobile Telecommunications System (1)
Architecture is an evolution of GSM; terminology differs
Packets goes to/from the Internet via SGSN/GGSN
Internet

## Slide 61: LTE
Voice calls are digital as well
Peak downlink: 86 Mbps  325 Mbps

## Slide 62: Learned today
Principal bandwidth limits
  Nyquist’s and Shannon’s theorems
Cable vs Wifi, fiber and satellite
Modulation: Encoding of binary signals in electric waves
Structure of the phone network, DSL and mobile network