## Slide 1: Distributed Systems 4. Data Link Layer
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2016/2017

## Slide 2: The Data Link Layer
Responsible for delivering frames of information over a single link
  Handles transmission errors and regulates the flow of data
Physical
Link
Network
Transport
Application

## Slide 3: The Data Link Layer
  Framing
  Error Detection and Correction
  Example Data Link Protocols

## Slide 4: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Actual data path
Virtual data path
Network
Link
Physical

## Slide 5: Possible Services
Unacknowledged connectionless service
  Frame is sent with no connection / error recovery
  Ethernet is example
Acknowledged connectionless service
  Frame is sent with retransmissions if needed
  Example is 802.11 (WiFi)
Connection-oriented service
  Not in this layer

## Slide 6: What is Framing, and why?

## Slide 7: Framing Methods
  Byte count for frames
  Flag bytes with byte stuffing
  Physical layer coding violations

## Slide 8: Framing – Byte count for frames
Frame begins with a count of the number of bytes in it
  Simple, but difficult to resynchronize after an error
Error
case
Expected
case

## Slide 9: Framing – Byte stuffing
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
Stuffing
examples
Frame
format
Need to escape extra ESCAPE bytes too!

## Slide 10: Your turn
What are the frames that were sent?
FLAG A B ESC FLAG C FLAG FLAG ESC ESC ESC FLAG D F ESC FLAG A ESC ESC FLAG FLAG B ESC FLAG D B FLAG

## Slide 11: Framing – Physical coding violation
How?

## Slide 12: The Data Link Layer
  Framing
  Error Detection and Correction
  Example Data Link Protocols

## Slide 13: Error Detection and Correction
Two basic strategies:
Correct errors at receiver side (using error-correcting codes)
Detect errors at receiver side and request retransmission
Preferred method depends on the error probability
  E.g. fiber: Error detection + retransmission
  E.g. Wifi: Error correcting codes

## Slide 14: FFFooouuunnndddaaatttiiiooonnn ooofff EEErrrrrrooorrr CCCooonnntttttrrrooolll: RRReeeddduuunnndddaaannncccyyy
AABsss yyyooouux cccaaanmn ssseeeaee, rrreeeddduuunnndddaaannncccyyy aaallllllouowwwsss tttooo ddteeettdeeekccttt aaannmddd cccooorrrrrreeecccttt sssmmnaaallllll eeerrgrrrooorrrsss,

## Slide 15
Dd y knw: Natrl langge cntns a lt f rdndncy. Ths s th rsn tht w cn ndrstnd each otr evn in nsy nvrnmnts

## Slide 16: Error Codes
Error codes add structured redundancy to data so errors can be either detected, or corrected.
Error detection codes:
  Parity
  Checksums
  Cyclic redundancy codes (CRC)
Error correction codes:
  Hamming codes
  Reed-Solomon and Low-Density Parity Check codes
    Mathematically complex, widely used in real systems

## Slide 17: Error Detection – Parity
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110 000  1110 0001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 1110 0101; detected, sum is wrong
  Ex: 3 errors, 1101 1001; detected sum is wrong
  Ex: 2 errors, 1110 1101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½

## Slide 18: Error Detection – Checksums
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: IPv4 protocol uses 16-bit checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Detects random errors with probability 1-(1/2)N
  Vulnerable to systematic errors, e.g., added zeros

## Slide 19: Error Detection – CRCs (1)
Adds bits so that transmitted frame evenly divisible by a fixed divisor
E.g., with divisor=23: Message Checksum (2 digits)
95
7342
18572965
CRCs do that on the level of polynoms
 1011 = x4+x2+x

## Slide 20: Error Detection – CRCs (2)
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits (hardware)
Stronger detection than checksums:
  E.g., can detect all double bit errors
  Not vulnerable to systematic errors

## Slide 21: Richard Hamming (1915-1998)
1915-1998
American mathematician
Worked on the Manhattan project
Influence on foundations of communication and networking

## Slide 22: Error Bounds – Hamming distance
Code turns data of n bits into codewords of n+k bits
Hamming distance is the minimum bit flips to turn one valid codeword into any other valid one.
  Example with 4 codewords of 10 bits (n=2, k=8):
    000000000000, 010000011111, 101111100000, and 111111111111
    Hamming distance is 5
Bounds for a code with distance:
  2d+1 – can correct d errors (e.g., 2 errors above)
  d+1 – can detect d errors (e.g., 4 errors above)

## Slide 23: Error Correction – Hamming code
Hamming code gives a simple way to add check bits and correct up to a single bit error:
  Check bits are parity (XOR) over subsets of the codeword
  Recomputing the parity sums (syndrome) gives the position of the error to flip, or 0 if there is no error
  (7,4) Hamming code for (d1,d2,d3,d4,p1,p2,p3)-ordering p1 = d1⊕d2⊕d3 p2 = d2⊕d3⊕d4 p3 = d3⊕d4⊕d1
  Let’s encode 1001 and 0101
p1
d3
p2
p3
d1
d2
d4

## Slide 24
0100 110 1001 110
0001 101 0000 000
0111 010 0110 001
1011 100 0110 001
Decode the following four ASCII characters

## Slide 25: Hamming Codes - Generalization
d data bits
r check bits
Values for d and r that satisfy the following equation allow to correct one error:
d+r+1 ≤ 2r

## Slide 26: Notes
Assignment
  Namen in PDF und Kommentar in Code
  Input: String  Char[] … Char  Byte  Bits
Sprache
  …

## Slide 27: Hamming code vs Gray code
?

## Slide 28: Error Detection: IBANs
http://www.ibancalculator.com/
Example:
bank code 123456, bank abbreviation WEST
account number 98765432
Redundancy is in blue
IBAN: |  | GB82 WEST 1234 5698 7654 32 | 
• Rearrange: |  | W E S T12345698765432 G B82 | 
• Convert to integer (A=10, ..) |  | 3214282912345698765432161182 | 
• Compute remainder: |  | 3214282912345698765432161182 | mod 97 = 1

## Slide 29: The Data Link Layer
  Framing
  Error Detection and Correction
  Example Data Link Protocols

## Slide 30: Example Data Link Protocols
  Packet over SONET »
  PPP (Point-to-Point Protocol) »
  ADSL (Asymmetric Digital Subscriber Loop) »

## Slide 31: PPP
IP packet
0x21 for IPv4
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
  Used e.g. to carry IP packets over fibers, or in ADSL
  Framing uses a flag (0x7E) and byte stuffing
  Connectionless unacknowledged service is used for IP packets
  Errors are detected with a checksum

## Slide 32: ADSL (1)
Widely used for broadband Internet over local loops
  ADSL runs from modem (customer) to DSLAM (ISP)
  IP packets are sent over PPP and AAL5/ATM (53 byte frame length)

## Slide 33: ADSL (2)
PPP data is sent in AAL5 frames over ATM cells:
  ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
  AAL5 is a format to send packets over ATM
  PPP frame is converted to a AAL5 frame (PPPoA)

## Slide 34: Learned today
Why framing is needed and how it can be done with byte stuffing
Redundancy and Hamming distance
(7,4)-Hamming code
Next
  How to share a link (=Medium access control sublayer)
  Assignment due Monday 20th: Hamming-code implementation