## Slide 1: Distributed Systems 9. Network Layer in the Internet
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2016/2017

## Slide 2: The Network Layer
Remember:
Responsible for delivering packets between endpoints over multiple links
(Link layer: single link Transport layer: Uses this service)
Physical
Link
Network
Transport
Application

## Slide 3: Outline
  IP Version 4
  IP Addresses
  IP Version 6
  Internet Control Protocols
  Label Switching and MPLS
  OSPF—An Interior Gateway Routing Protocol
  BGP—The Exterior Gateway Routing Protocol

## Slide 4: Network Layer in the Internet
Internet is an interconnected collection of many networks that is held together by the IP protocol

## Slide 5: IP Version 4 Protocol (1)
IPv4 (Internet Protocol) header is carried on all packets and has fields for the key parts of the protocol:

## Slide 6: Wireshark

## Slide 7: Hierarchical Routing – Classful Addresing
Old addresses came in blocks of fixed size (A, B, C)
  Carries size as part of address, but lacks flexibility
  Called classful (vs. classless) addressing
   Router need only one entry per external subnet

## Slide 8: IP Addresses (1) – Prefixes
Addresses are allocated in blocks called prefixes
  Prefix is determined by the network portion
  Written address/length, e.g., 18.0.31.0/24

## Slide 9: IP Addresses (2) – Subnets
Subnetting splits up IP prefix to help with management
  Looks like a single prefix outside the network
Network divides it into subnets internally
ISP gives network
a single prefix

## Slide 10: Your turn
Subnet A has address 141.89.228.0/26
How many addresses are in this subnet?
What is the lowest, what is the highest address in this subnet?
Computer B has the IPv4 address (including the subnet mask in CIDR notation) 141.89.228.65/26.
Computer C is reachable as 141.89.228.63/26.
Do they belong to the same subnet?

## Slide 11: IP Version 6 (1)
Major upgrade in the 1990s due to impending address exhaustion, with various other goals:
    Support billions of hosts
    Simpler protocol
    Better security
    Attention to type of service
    Allow future protocol evolution
Deployment has been slow & painful, but is expected to pick up pace
  6/2016: All IPv4 spaces except Africa are exhausted (Source: http://www.networkcomputing.com/networking/ipv6-progress-report-going-mainstream/1699620417)
  IPv6 Adoption: https://www.google.com/intl/en/ipv6/statistics.html
  Machine check: http://test-ipv6.com/

## Slide 12: How many addresses?
Three hundred and forty undecillion, two hundred and eighty-two decillion, three hundred and sixty-six nonillion, nine hundred and twenty octillion, nine hundred and thirty-eight septillion, four hundred and sixty-three sextillion, four hundred and sixty-three quintillion, three hundred and seventy-four quadrillion, six hundred and seven trillion, four hundred and thirty-one billion, seven hundred and sixty-eight million, two hundred and eleven thousand, four hundred and fifty-six.

## Slide 13: IP Version 6 (2 )
IPv6 protocol header has much longer addresses (128 vs. 32 bits) and is simpler (by using extension headers)
Extensions allow encryption, authentication, routing preferences, ….

## Slide 14: Internet Control Protocols (1)
IP works with the help of several control protocols:
  ICMP is a companion to IP that returns error info
    Required, and used in many ways, e.g., for traceroute
  ARP finds Ethernet address of a local IP address
    Glue that is needed to send any IP packets
    Host queries an address and the owner replies
  DHCP assigns a local IP address to a host
    Gets host started by automatically configuring it
    Host sends request to server, which grants a lease

## Slide 15: Internet Control Protocols (3)
ARP (Address Resolution Protocol) lets nodes find target Ethernet addresses [pink] from their IP addresses
Broadcast: “Who has IP X?”
Router takes all external addresses

## Slide 16: OSPF— Interior Routing Protocol
OSPF (Open Shortest Path First) computes routes for a single network (e.g., ISP)
  Models network as a graph of weighted edges
Network:
Graph:
OSPF is link-state routing:
  Uses messages below to reliably flood topology
  Then runs Dijkstra to compute routes

## Slide 17: BGP— Exterior Routing Protocol (1)
BGP (Border Gateway Protocol) computes routes across interconnected, autonomous networks
  Key role is to respect networks’ policy constraints
Example policy constraints:
    No commercial traffic for educational network
    Never put Iraq on route starting at Pentagon
    Choose cheaper network
    Choose better performing network

## Slide 18: Learned today
Internet Protocol (IP)
  Network address + host address
  IPv4 vs IPv6
  ARP for finding MAC addresses
Internet
  OSPF inside a network
  BGP between networks
IP Simulation: http://www.cs.stir.ac.uk/~kjt/software/comms/jasper/IP.html