## Slide 1: Distributed Systems 7. Network Layer Theory
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2016/2017

## Slide 2: Notes
CSMA not slotted
  slotting is rather difficult
  ALOHA could do it presumably because of long frames

## Slide 3: Network Layer
  Design Issues
  Routing Algorithms
    Distance vector
    Link state routing
  Congestion Control
  Quality of Service

## Slide 4: The Network Layer
Service: Delivering packets between endpoints over multiple links
Which service does it use from the link layer?
Physical
Link
Network
Transport
Application

## Slide 5: Core function: Forward Packet Switching
Hosts send packets into the network; packets are forwarded by routers
ISP’s equipment
    Connectionless service – datagrams
    Connection-oriented service – virtual circuits

## Slide 6: Connectionless Service – Datagrams
Packet is forwarded using destination address inside it
  Different packets may take different paths
ISP’s equipment
A’s table (initially) A’s table (later) C’s Table E’s Table
Dest. Line
Routing tables:
B
B

## Slide 7: Connection-Oriented – Virtual Circuits
Packet is forwarded along a virtual circuit using tag inside it
  Virtual circuit (VC) is set up ahead of time
ISP’s equipment
A’s table C’s Table E’s Table
In: Line Tag
Line Tag: Out

## Slide 8: Comparison of Virtual-Circuits & Datagrams

## Slide 9: 7. Network Layer
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service

## Slide 10: Routing Algorithms (1)
  Dijkstra’s Shortest path algorithm
  Distance vector routing
  Link state routing
  Hierarchical routing
  Routing for mobile hosts

## Slide 11: Routing Algorithms (2)
Routing is the process of discovering network paths (creating a routing table)
  Model the network as a graph of nodes and links
  Decide what to optimize (e.g., fairness vs efficiency, bandwidth vs delay)
Forwarding is the sending of packets along a path, using routing tables

## Slide 12: Shortest Path Algorithm (2)
A network and first five steps in computing the shortest paths from A to D. Pink arrows show the sink tree so far.

## Slide 13: Shortest Path Algorithm (1)
Dijkstra’s algorithm computes shortest path to all nodes from one node in a graph
Foundations:
    Each link is assigned a non-negative weight/distance
    Shortest path is the one with lowest total weight
    Using weights of 1 gives paths with fewest hops
Algorithm:
    Start with source, set distance to other nodes to infinity
    Update distances to reachable nodes
    Pick the lowest distance node, add it to set of visited nodes
    Repeat until all nodes are visited

## Slide 14: Your turn
Shortest paths from A?

## Slide 15: Dijkstra’s algorithm is nice, but…
…how do we actually compute it?
Decentralized (Distance vector routing)
Centralized (Link state routing)

## Slide 16: Distance Vector Routing (1)
Distance vector is a distributed routing algorithm
  Shortest path computation is split across nodes
Algorithm:
  Each node knows distance of links to its neighbors
  Each node advertises vector of lowest known distances to all neighbors
  Each node uses received vectors to update its own
  Repeat periodically

## Slide 17: Distance Vector Routing (2)
Network
Vectors received at J from
Neighbors A, I and H
New vector for J

## Slide 18: The Count-to-Infinity Problem
Failures can cause DV to “count to infinity” while seeking a path to an unreachable node
Good news of a path to A spreads quickly
X
Bad news of no path to A is learned slowly
+

## Slide 19: Link State Routing (1)
Link state is an alternative to distance vector
  More computation but simpler dynamics
  Widely used in the Internet (OSPF, IS-IS)
Algorithm:
  Each node floods information about its neighbors in LSPs (Link State Packets); all nodes learn the full network graph
  Each node runs Dijkstra’s algorithm to compute the path to take for each destination
  How can we send LSPs to all nodes?
    No broadcast functionality in WANs
    Simple flooding can lead to exponential blowup

## Slide 20: Link State Routing (2) – LSPs
LSP (Link State Packet) for a node lists neighbors and weights of links to reach them
Network?
LSP for each node

## Slide 21: Link State Routing (3) – Reliable Flooding
Seq. number and age are used for reliable flooding
  New LSPs are acknowledged on the lines they are received and sent on all other lines
  Example shows the LSP database at router B

## Slide 22: Distance Vector vs. Link State Routing
 | Distance Vector Routing | Link State Routing
Functionality |  | 
Message Content |  | 
Message Number |  | 
Challenge |  | 

## Slide 23: Size of routing tables for the internet
IPv4: 32-bit addresses
IPv6: 128-bit addresses
 ?

## Slide 24: Hierarchical Routing
Hierarchical routing reduces the work of route computation but may result in slightly longer paths than flat routing
Best choice to reach nodes in 5 except for 5C

## Slide 25: Routing for Mobile Hosts
Mobile hosts can be reached via a home agent
  Fixed home agent tunnels packets to reach the mobile host; reply can optimize path for subsequent packets
  No changes to routers or fixed hosts

## Slide 26: Assignment 1
Limited teamwork
Make PDF
IDE is an overkill
References!
Structuring…

## Slide 28
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service

## Slide 29: Congestion Control (1)
Handling congestion is the responsibility of the Network and Transport layers working together
    We look at the network portion here

## Slide 30: Congestion Control (2)
Congestion results when too much traffic is offered; performance degrades due to loss/retransmissions
  Goodput (=useful packets) trails offered load

## Slide 31: What can be done?

## Slide 32: Congestion Control (3) – Approaches
Network must do its best with the offered load
  Different approaches at different timescales
  Nodes should also reduce offered load (Transport)

## Slide 33: Traffic-Aware Routing
Choose routes depending on traffic, not just topology
  E.g., use EI for West-to-East traffic if CF is loaded
  But take care to avoid oscillations

## Slide 34: Admission Control
Admission control allows a new traffic load only if the network has sufficient capacity, e.g., with virtual circuits
  Can combine with looking for an uncongested route
Network with some congested nodes
Uncongested portion and route AB around congestion

## Slide 35: Traffic Throttling
Congested routers signal hosts to slow down traffic
  ECN (Explicit Congestion Notification) marks packets and receiver returns signal to sender

## Slide 36: Load Shedding (1)
When all else fails, network will drop packets (shed load)
Which packets to throw away?
 Milk-or-wine problem

## Slide 37
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service

## Slide 38: Application Requirements (1)
Different applications care about different properties
  We want all applications to get what they need
.
“High” means a demanding requirement, e.g., low delay

## Slide 39: How can we make guarantees?
Traffic shaping regulates the average rate and burstiness of data entering the network
  Allows to give guarantees
Shape traffic here

## Slide 40: Traffic Shaping: Token Bucket
Token bucket limits both the average rate (R) and short-term burst (B) of traffic
  Bucket size is B, water enters at rate R and is removed to send
   See demonstration

## Slide 41: Traffic Shaping: Token Bucket (2)
Shaped by R=25 MB/s B=9,6 MB
Shaped by R=25 MB/s B=0 KB
Host traffic
Smaller bucket size delays traffic and reduces burstiness
How much is sent How much can be sent

## Slide 42: Example
Router with three inputs A, B and C, and one output, D, and 100 MB internal memory
- A has token bucket with R= 10 Mbit/s, size 40 MB
- B has token bucket with R= 20 Mbit/s, size 70 MB
- D has token bucket with R= 55 Mbit/s, size 50 MB
- C would like token bucket with R=10 Mbit/s, size 60 MB
Can C’s wish be satisfied?

## Slide 43: Buckets in series
A single token bucket may allow strong bursts
Put smaller buckets with higher rate behind
Token bucket with B=0 is called leaky bucket

## Slide 44: Learned today
Connectionless vs connection-oriented routing
Routing
  Distance vector
    Problem: Count to infinity
  Link state
    Challenge: Information propagation
Techniques for congestion control
Traffic shaping: Token-bucket