## Slide 1: Distributed Systems 3. Protocol Hierarchies, OSI and TCP/IP
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2014/2015

## Slide 2: Network Hardware
Networks can be classified by their scale:
Scale | Type
Vicinity | PAN (Personal Area Network) »
Building | LAN (Local Area Network) »
City | MAN (Metropolitan Area Network) »
Country | WAN (Wide Area Network) »
Planet | The Internet (network of all networks)

## Slide 3: Personal Area Network
Connect devices over the range of a person
Example of a Bluetooth (wireless) PAN:

## Slide 4: Local Area Networks
Connect devices in a home or office building
Called enterprise network in a company
Wireless LAN
with 802.11
Wired LAN with
switched Ethernet

## Slide 5: Metropolitan Area Networks
Connect devices over a metropolitan area
Example MAN based on cable TV:

## Slide 6: Wide Area Networks (1)
Connect devices over a country
Example WAN connecting three branch offices:

## Slide 7: Wide Area Networks (2)
An ISP (Internet Service Provider) network is also a WAN.
Customers buy connectivity from the ISP to use it.

## Slide 8: Wide Area Networks (3)
A VPN (Virtual Private Network) is a WAN built from virtual links that run on top of the Internet.

## Slide 9: Network Software
Protocols

## Slide 10: Protocol
Agreement between communicating parties (peers) on how communication is to proceed
  Peer: processes, devices, humans, …
  Defines
    Syntax: the format of messages
      Flag positions, 0-12V, 101001, A-Z
    Interaction: the order of messages
    Semantics: meaning of exchanged data and actions to be executed when a message is received

## Slide 11: Protocol Stack
Complexity of networks  layered organization
  Separation of duties and responsibilities
  Decomposition
  Decoupling
Layer N
  Offers certain services to layer N+1
  Hides how these services are implemented
  Exploits services made available by layer N-1
Protocol stack: each layer virtually communicates with the corresponding remote layer

## Slide 12: Layers, Protocols, Interfaces
Interface: primitive operations and services made available by a layer to the upper one

## Slide 13: Layers, Protocols, Interfaces
Interface: primitive operations and services made available by a layer to the upper one

## Slide 14: Layers, Protocols, Interfaces
Interface: primitive operations and services made available by a layer to the upper one

## Slide 15: Multilayer Communication

## Slide 16: Example
Interaction between philosophers – Service offerings
  Philosopher layer (philosophical notions)
  Translation layer (from/to dutch)
  Secretary layer (send/receive letter to/from fax number)
  Hardware layer (fax sent over telephone infrastructure)
    Could also be by email, mail, flag signals

## Slide 17: User Interaction
User layer (text, images, music, documents, voice, video)
...
...
...
…
Physical layer (electric/radio signals, …)
?

## Slide 18: Virtual vs Real Communication
Layer 5: conceptual horizontal communication (send M to …)
Layer 4: header for …?
Layer 3: deals with space limits  message packets
Headers/trailers are not seen by layer 5

## Slide 19: Protocol vs Service
Service: operations offered by a layer to the upper one
  Lower layer: service provider (delegation)
  Upper layer: service consumer (abstraction)
  Interface between the two layers
Protocol: governs the interaction between peers, defining the format and meaning of exchanged messages
Service implementation may rely on a protocol (not visible to service consumer)

## Slide 20: Protocol Requirements
Addressing
  Many machines, many processes  identification of the recipient of a message
Error control
  Physical communication circuits are not perfect
  Agreement on the control mechanism is needed
  Packets can be out-of-order  reassembling capabilities in the destination
Flow control
  Feedback from receiver to sender
Multiplexing/demultiplexing
  Management of the same connection for multiple conversations
Routing
  Best path for reaching the destination

## Slide 21: Connection(less) Service
Remember C/S?
Connection-oriented service: creation of a virtual end-to-end communication channel
  Order preservation
  E.g. the telephone system
  Three phases
    Connection establishment and negotiation
    Use of the connection
    Connection release
Connectionless service: fragmentation of interaction into separate messages
  Each message carries the full destination address
  Each message follows a route  possibility of out-of-order messages
  E.g. the postal system

## Slide 22: Quality of Service
Measure the reliability of the service
  N.B.: the physical medium is in general unreliable!
Reliability requires additional interaction (ack)
  Computational overload (delays)
Reliable connection-oriented service
  Message sequence: messages preserved (scan of a book)
  Byte stream: no message boundaries (remote login)
Reliability is not always feasible/reasonable
  Digitized voice  delays unacceptable
  File transfer: necessary
Reliable connectionless service
  Acknowledged datagram service (ack of message reception)
  Request-reply service
Unreliable connectionless service: Ethernet

## Slide 23: Types of Services
Remember: reliability is not always feasible nor desired

## Slide 24: Service Primitives
Primitives: tell the service to do some action
  Protocol stack in the O.S.  system calls
  Captured by the kernel, which then sends the packets
Primitives depend on the type of service
E.g., primitives for reliable byte stream:

## Slide 25: C/S Interaction with Connection-Oriented Network
Faults and errors must be managed
  Graceful degradation is a must

## Slide 26: From Abstract to Concrete Models
Abstract model: layered model with services, protocols, interfaces
Concrete model: fixes # layers, content and function of each layer
Two fundamental models
  ISO OSI reference model
    “top-down” (good model)
  TCP/IP
    “bottom-up” (widely used protocols)

## Slide 27: OSI Reference Model
Open System Interconnection (1983, revised 1995)
  Targets open systems: systems that are open for communication with other systems
  Interoperability: its goal is to enable cooperation of heterogeneous systems
Well-defined layers
Object-oriented
Abstract model: not bound to specific implementations/vendors

## Slide 28: OSI As a Standard
Driven by ISO (International Organization for Standardization)
With the contribution of
  IEC (International Electrotechnical Commission)
  CCITT (International Telegraph and Telephone Consultative Committee)
  Industrial organizations
    ECMA (European Computer Manufacturers' Association)
    IEEE (Institute of Electrical and Electronics Engineers)
    EIA (Electronic Industries Association)

## Slide 29: OSI Reference Schema
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
Physical Medium
HOST 1
Application
Presentation
Session
Transport
Network
Data link
Physical
HOST 2
A-protocol (APDU)
P-protocol (PPDU)
S-protocol (SPDU)
T-protocol (TPDU)
N-protocol (packet)
D-protocol (frame)
Ph-protocol (bit)
P-Interface
S-interface
T-interface
N-interface
D-interface
Ph-interface

## Slide 30: OSI Layers - Guidelines
A layer should be created where a different abstraction is needed.
Each layer should perform a well-defined function.
The function of each layer should be chosen with an eye toward defining internationally standardized protocols.
The layer boundaries should be chosen to minimize the information flow across the interfaces.
The number of layers should be large enough that distinct functions need not be thrown together in the same layer out of necessity and small enough that the architecture does not become unwieldy.

## Slide 31: Information Encapsulation
Service Data Unit (SDU): actual data at level N
  In the application layer: user’s data
Protocol Data Unit (PDU): unit of information exchanged via some protocol
  PDU(N) = PCI(N) + SDU(N)
  Protocol Control Information (PCI): protocol-related parameters
    Service provider’s identifier
Interface Data Unit (IDU): unit of information vertically passed to the underlying layer
  IDU(N-1) = ICI(N) + PDU(N)
  Interface Control Information (ICI): interface-related parameters used to “call” the underlying service
  Level N-1 extracts the ICI(N) part, while SDU(N-1) = PDU(N)

## Slide 32: Encapsulation - Sketch

## Slide 33: Encapsulation - Description
The layer-n entity passes an interface data unit (IDU) to the layer-(n–1) entity
The IDU consists of a protocol data unit (PDU) and some interface control information (ICI)
  The ICI is information, such as the length of the SDU, and the addressing information that the layer below needs to perform its function.
The PDU is the data that the layer-n entity wishes to pass across the network to its peer entity
  It consists of the layer-n header and the data that layer n received from layer (n+1).
The layer-n PDU becomes the layer-(n–1) service data unit (SDU), because it is the data unit that will be serviced by layer n.
When layer n–1 receives the layer-n IDU, it strips off and "considers" the ICI, adds the header information for its peer entity across the network, adds ICI for the layer below, and passes the resulting IDU to the layer n–2 entity.
Problems can occur in the data path between two network stations, including errant, restricted, or even halted communication.

## Slide 34: Information Encapsulation

## Slide 35: OSI - Dataflow

## Slide 36: OSI – Interaction Modalities
Connectionless: every SDU managed independently from the others
  No guaranteed QoS
  No memory nor negotiation, just isolated communication
Connection-oriented: connection set up between peers, whose features are negotiated at the beginning
  QoS and support for the three interaction phases
  N.B.: connection maintained by the peers but not necessarily by the intermediate nodes

## Slide 37: OSI - Primitives
7 Layers
3 types of primitives:
  Data: transmission of content
  Connect: opens connection (not used in the connectionless case)
  Disconnect: closes connection (not used in the connectionless case)
4 forms for a primitive:
  Request: (requesting) service user requests a service (action)
  Indication: service provider notifies the (accepting) service user that a service has been requested
  Response: service user provides an answer to a request-for-service
  Confirm: service provider sends back the response related to arequest-for-service
Primitive: <LAYER>-<PRIMITIVE TYPE>.<PRIMITIVE FORM>
  E.g.: S-connect.response

## Slide 38: OSI – Interaction Patterns
Asynchronous
(no confirm)
(N)-Service User
(N)-Service Provider
(N)-Service User
t
  N-Type.REQUEST
  N-Type.INDICATION
Service not confirmed
Synchronous
Result to client,
with confirm
  N-Type.REQUEST
  N-Type.INDICATION
Service confirmed
  N-Type.RESPONSE
  N-Type.CONFIRM
Blocking asynchrounous
Only confirm
  N-Type.REQUEST
  N-Type.INDICATION
Service partially confirmed
  N-Type.CONFIRM

## Slide 39: OSI Layers 1-2
Physical layer
  Transmission of raw bits over a communication channel
  Decisions on mechanical, electrical, timing issues
  Use of the physical transmission medium below
Data Link
  Transforms a raw transmission facility into a “transmission errors-free” communication line
  Data break up in fragments (~100(0) b) transmitted sequentially

## Slide 40: OSI Layer 3 - Network
Goal: moving messages through the network
  Splits information in packets
Visibility of intermediate nodes: routing strategies and addressing
  Flow control (peers): avoid overload on the reveicer
  Congestion control (network): avoid bottlenecks
  Fairness
node

## Slide 41: OSI Layer 4 - Transport
Receives data from the above, splits it up into smaller units that are then passed to the network layer
Separates the “user/application layers” (above) from the “communication layers” (below)
First layer that virtually connects the two end-points directly
Determines the main features underlying users’ interaction: reliability, ordering of messages, connection(less) interaction,…

## Slide 42: OSI Layer 4 - Transport
Decomposes and reassembles data
  Independently from the network layer
  Multiplexing to recombine the whole info

## Slide 43: OSI Layer 4 - Connection
Typical T-interaction modality: connection-oriented
Minimal interaction primitives
  T-CONNECT
    At least source and destination address
    Service with confirmation
  T-DATA
  T-DISCONNECT

## Slide 44: Separation Principle
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
HOST 1
HOST 2
Application
Presentation
Session
Transport
Network
Data link
Physical
Network
Data link
Physical
Network
Data link
Physical
Separation
Interconnection network
user/application protocols

## Slide 45: History of the Internet
https://www.youtube.com/watch?v=9hIQjrMHTv4
(8 minutes)

## Slide 46: The Internet
A network of networks
Emerged in a bottom-up way
Composed of a set of layers and protocols that became de-facto standards
  TCP/IP
  Not completely aligned with OSI reference model
Born from ARPANET

## Slide 47: Internet Evolution

## Slide 48: Birth of Internet
Late 1950s  USA Department of Defense feared the Cold War
Military communications: public telephone network
  Vulnerable!
Need for a resilient network for military communications

## Slide 49: Baran’s Network
  Paul Baran’s distributed fault-tolerant network
    Based on packet switching
  In the meanwhile, ARPA was created: Advanced Research Projects Agency

## Slide 50: ARPANET
1967: Roberts and Clarks developed a packet-switching
  Cited Baran
  IMP: mini-computers with dynamic routing support

## Slide 51: Growth of ARPANET (’69-’72)

## Slide 52: TCP/IP
With the growth of ARPANET, it became clear that its protocols were not suited to deal with heterogeneous networks
1974: Cherf and Kahn design TCP/IP
  Specifically tailored to internetworking!
Sockets developed at Berkeley as an API to the network
Rapid growth of ARPANET
  Connection of many LANs
DNS to map logical names to IP addresses
U.S. National Science Foundation creates NSFNET to connect universities
  Connected to ARPANET

## Slide 53: TCP/IP Reference Model
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
OSI
TCP/IP
Application
Transport
Internet
Host-to-network

## Slide 54: TCP/IP Host-to-Network
Usually left almost completely unspecified
Minimal requirement:
  Ability to connect host to network
  Injection of packets
Varies from network to network
We can take the OSI reference model for the physical layer + data link

## Slide 55: Internet Layer
Connectionless layer supporting
  The injection of packets in any network
  The routing to the destination, possibly across networks
Internet layer like a mail system
Official packet format and transmission protocol: IP (Internet Protocol)
  “Universal” envelope for information

## Slide 56: Transport Layer
Supports conversations between endpoints
Two protocols
  TCP (Transmission Control Protocol)
    Reliable connection-oriented byte stream
    At-most-one semantics
  UDP (User Datagram Protocol)
    Unreliable connectionless protocol
    No sequencing
    May-be semantics

## Slide 57: Application Layer
On top of the transport layer
  Practical experience showed that presentation+session are of little use
Application-level protocols
  Virtual terminal (TELNET)
  File transfer (FTP)
  E-mail (SMTP)
  Naming (DNS)
  World wide web (HTTP)

## Slide 58: OSI vs TCP/IP
Both are multi-layered
OSI: provides a clear separation of services, interfaces, protocols
  Defined “before” protocols
  Far from reality
TCP/IP: no clear distinction among these three concepts
  Fixed protocols
  Model just describes the existing protocols

## Slide 59: Take home
Protocol stack
  protocols provide services to higher-level protocols
  use lower-level protocols