## Slide 1: Distributed Systems 4. Physical Layer
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2014/2015

## Slide 2: The Physical Layer
  Theoretical Basis for Data Communications
  Guided Transmission Media
  Wireless Transmission
  Communication Satellites
  Digital Modulation and Multiplexing
  Public Switched Telephone Network
  Mobile Telephone System

## Slide 3: The Physical Layer
Foundation on which other layers build
  Properties of wires, fiber, wireless limit what the network can do
Key problem is to send (digital) bits using only (analog) signals
  This is called modulation
Physical
Link
Network
Transport
Application

## Slide 4: Theoretical Basis for Data Communication
Communication rates have fundamental limits
  Fourier analysis »
  Bandwidth-limited signals »
  Maximum data rate of a channel »

## Slide 5: Fourier Analysis
A time-varying signal can be equivalently represented as a series of frequency components (harmonics):
a, b weights of harmonics
Signal over time
=

## Slide 6: Bandwidth-Limited Signals
Having less bandwidth (harmonics) degrades the signal
8 harmonics
4 harmonics
2 harmonics
Lost!
Bandwidth
Lost!
Lost!

## Slide 7: Maximum Data Rate of a Channel
Nyquist’s theorem (1924) relates the data rate to the bandwidth (B) and number of signal levels (V):
 Maximum data rate of a binary of a binary signal over a 3kHz channel is 6000bps
Max. data rate = 2B log2V bits/sec
How fast signal
can change
How many levels
can be seen

## Slide 8: Visualization
http://www.intmath.com/fourier-series/fourier-graph-applet.php

## Slide 9: Technologies

## Slide 10: Wires – Twisted Pair
Very common; used in LANs, telephone lines
  Twists reduce radiated signal (interference)
Category 5 UTP cable with four twisted pairs

## Slide 11: Wires – Coaxial Cable (“Co-ax”)
Also common. Better shielding and more bandwidth for longer distances and higher rates than twisted pair.

## Slide 12: Wires – Power Lines
Household electrical wiring is another example of wires
  Convenient to use, but horrible for sending data

## Slide 13: Fiber Cables (1)
Common for high rates and long distances
  Long distance ISP links, Fiber-to-the-Home
  Light carried in very long, thin strand of glass
Light source
(LED, laser)
Photodetector
Light trapped by
total internal reflection

## Slide 14: Fiber Cables (2)
Fiber has enormous bandwidth (THz) and tiny signal loss – hence high rates over long distances
3 dB = half point of energy

## Slide 15: Fiber Cables (3)
Single-mode
  Core so narrow (10um) light can’t even bounce around
  Used with lasers for long distances, e.g., 100km
Multi-mode
  Other main type of fiber
  Light can bounce (50um core)
  Used with LEDs for cheaper, shorter distance links
Fibers in a cable

## Slide 16: Fiber Cables (4)
Comparison of the properties of wires and fiber:
Property | Wires | Fiber
Distance | Short (100s of m) | Long (tens of km)
Bandwidth | Moderate | Very High
Cost | Inexpensive | Less cheap
Convenience | Easy to use | Less easy
Security | Easy to tap | Hard to tap

## Slide 17: Wireless Transmission
  Electromagnetic Spectrum »
  Radio Transmission »
  Microwave Transmission »
  Light Transmission »
  Wireless vs. Wires/Fiber »

## Slide 18: Electromagnetic Spectrum (1)
Different bands have different uses:
    Radio: wide-area broadcast; Infrared/Light: line-of-sight
    Microwave: LANs and 3G/4G;
Microwave
Networking focus

## Slide 19: Electromagnetic Spectrum (2)
To manage interference, spectrum is carefully divided, and its use regulated and licensed, e.g., sold at auction.
Source: NTIA Office of Spectrum Management, 2003
3 GHz
30 GHz
3 GHz
300 MHz
WiFi (ISM bands)
Part of the US frequency allocations

## Slide 20: Electromagnetic Spectrum (3)
Fortunately, there are also unlicensed (“ISM”) bands:
    Free for use at low power; devices manage interference
    Widely used for networking; WiFi, Bluetooth, etc.
802.11
b/g/n
802.11a/g/n

## Slide 21: Radio Transmission
In the HF band, radio waves bounce off the ionosphere.
In the VLF, LF, and MF bands, radio waves follow the curvature of the earth
Radio signals penetrate buildings well and propagate for long distances with path loss

## Slide 22: Microwave Transmission
Microwaves have much bandwidth and are widely used indoors (WiFi) and outdoors (3G, satellites)
  Signal is attenuated/reflected by everyday objects
  Strength varies due multipath fading, etc.

## Slide 23: Wireless vs. Wires/Fiber
Wireless:
    Easy and inexpensive to deploy
    Naturally supports mobility
    Naturally supports broadcast
    Transmissions interfere and must be managed
    Signal strengths hence data rates vary greatly
Wires/Fiber:
    Easy to engineer a fixed data rate over point-to-point links
    Can be expensive to deploy, esp. over distances
    Doesn’t readily support mobility or broadcast

## Slide 24: Communication Satellites
Satellites are effective for broadcast distribution and anywhere/anytime communications
  Kinds of Satellites »
  Geostationary (GEO) Satellites »
  Low-Earth Orbit (LEO) Satellites »
  Satellites vs. Fiber »

## Slide 25: Kinds of Satellites
Satellites and their properties vary by altitude:
  Geostationary (GEO), Medium-Earth Orbit (MEO), and Low-Earth Orbit (LEO)
Sats needed for global coverage

## Slide 26: Geostationary Satellites
GEO satellites orbit 35,000 km above a fixed location
    VSAT (computers) can communicate with the help of a hub
    Different bands (L, S, C, Ku, Ka) in the GHz are in use but may be crowded or susceptible to rain.
VSAT
GEO satellite

## Slide 27: Low-Earth Orbit Satellites
Systems such as Iridium use many low-latency satellites for coverage and route communications via them
The Iridium satellites form six necklaces around the earth.

## Slide 28: Satellite vs. Fiber
Satellite:
    Can rapidly set up anywhere/anytime communications (after satellites have been launched)
    Can broadcast to large regions
    Limited bandwidth and interference to manage
Fiber:
    Enormous bandwidth over long distances
    Installation can be more expensive/difficult

## Slide 29: Bandwidth
Internal/Home network/
Internet link
Connection | Speed |  |  | Transmit 1 GB
type | bps | B/sec |  | hh : mm : ss
56K Modem | 56 K | 6.8 K |  | 42 : 36 : 31.69
Classic DSL | 512 K | 62.5 K |  | 4 : 39 : 37.22
Cable | 10 M | 1.221 M |  | : 14 : 09.93
OC-1 | 51.840 M | 6.328 M |  | : 2 : 45.70
Ethernet | 100.00 M | 12.207 M |  | : 1 : 25.90
OC-3 | 155.52 M | 18.984 M |  | : : 55.23
OC-12 | 622.08 M | 75.937 M |  | : : 13.81

## Slide 30: Bandwidth is not everything..
7.1PB of storage (http://searchdatacenter.techtarget.com/review/Rackable-Systems-ICE-Cube-Modular-Data-Center)
transmission speed: 80 km/h
Bandwidth Rome-London (2kkm)?

## Slide 31: Digital Modulation and Multiplexing
Modulation schemes send bits as signals; multiplexing schemes share a channel among users.
  Baseband Transmission »
  Passband Transmission »
  Frequency Division Multiplexing »
  Time Division Multiplexing »
  Code Division Multiple Access »

## Slide 32: Baseband Transmission
Line codes send symbols that represent one or more bits
  NRZ is the simplest, literal line code (+1V=“1”, -1V=“0”)

## Slide 33: Clock Recovery
To decode the symbols, signals need sufficient transitions
  Otherwise long runs of 0s (or 1s) are confusing, e.g.:
Strategies:
  Manchester coding, mixes clock signal in every symbol
  4B/5B maps 4 data bits to 5 coded bits with 1s and 0s:
  Scrambler XORs tx/rx data with pseudorandom bits
1
0 0 0 0 0 0 0 0 0 0 um, 0? er, 0?
Data | Code | Data | Code | Data | Code | Data | Code
0000 | 11110 | 0100 | 01010 | 1000 | 10010 | 1100 | 11010
0001 | 01001 | 0101 | 01011 | 1001 | 10011 | 1101 | 11011
0010 | 10100 | 0110 | 01110 | 1010 | 10110 | 1110 | 11100
0011 | 10101 | 0111 | 01111 | 1011 | 10111 | 1111 | 11101

## Slide 34: Passband Transmission (1)
Modulating the amplitude, frequency/phase of a carrier signal sends bits in a (non-zero) frequency range
NRZ signal of bits
Amplitude shift keying
Frequency shift keying
Phase shift keying

## Slide 35: Passband Transmission (2)
BPSK
2 symbols
1 bit/symbol
QPSK
4 symbols
2 bits/symbol
QAM-16
16 symbols
4 bits/symbol
QAM-64
64 symbols
6 bits/symbol
QAM varies amplitude and phase
BPSK/QPSK varies only phase
Constellation diagrams are a shorthand to capture the amplitude and phase modulations of symbols:

## Slide 36: Passband Transmission (3)
Gray-coding assigns bits to symbols so that small symbol errors cause few bit errors:
A
B
C
D
E

## Slide 37: Frequency Division Multiplexing (1)
FDM (Frequency Division Multiplexing) shares the channel by placing users on different frequencies:
Overall FDM channel

## Slide 38: Time Division Multiplexing (TDM)
Time division multiplexing shares a channel over time:
  Users take turns on a fixed schedule; this is not packet switching or STDM (Statistical TDM)
  Widely used in telephone / cellular systems

## Slide 39: Code Division Multiple Access (CDMA)
CDMA shares the channel by giving users a code
  Codes are orthogonal; can be sent at the same time
  Widely used as part of 3G networks
A =
+1
-1
+1
-1
B =
+1
+1
-1
-1
+1
+1
-1
-1
C =
-2
+2
0
0
S = +A -B
S x A
+2
+2
-2
-2
-2
+2
0
0
S x B
S x C
Sum = 4
A sent “1”
Sum = -4
B sent “0”
Sum = 0
C didn’t send
Sender Codes
Transmitted
Signal
Receiver Decoding
0
0
0
0

## Slide 40: The Public Switched Telephone Network
  Structure of the telephone system »
  Politics of telephones »
  Local loop: modems, ADSL, and FTTH »
  Trunks and multiplexing »
  Switching »

## Slide 41: Structure of the Telephone System
A hierarchical system for carrying voice calls made of:
  Local loops, mostly analog twisted pairs to houses
  Trunks, digital fiber optic links that carry calls
  Switching offices, that move calls among trunks

## Slide 42: Local loop (1): modems
Telephone modems send digital data over an 3.3 KHz analog voice channel interface to the POTS
  Rates <56 kbps; early way to connect to the Internet

## Slide 43: Local loop (2): Digital Subscriber Lines
DSL broadband sends data over the local loop to the local office using frequencies that are not used for POTS
  Telephone/computers attach to the same old phone line
  Rates vary with line
    ADSL2 up to 12 Mbps
  OFDM is used up to 1.1 MHz for ADSL2
    Most bandwidth down

## Slide 44: Local loop (3): Fiber To The Home
FTTH broadband relies on deployment of fiber optic cables to provide high data rates customers
  One wavelength can be shared among many houses
  Fiber is passive (no amplifiers, etc.)

## Slide 45: Switching (1)
PSTN uses circuit switching; Internet uses packet switching
PSTN:
Internet:

## Slide 47: Strowger Switches (1891)

## Slide 48: Switching (2)
Circuit switching requires call setup (connection) before data flows smoothly
  Also teardown at end (not shown)
Packet switching treats messages independently
  No setup, but variable queuing delay at routers
Circuits
Packets

## Slide 49: Switching (3)
Comparison of circuit- and packet-switched networks

## Slide 50: Mobile Telephone System
  Generations of mobile telephone systems »
  Cellular mobile telephone systems »
  GSM, a 2G system »
  UMTS, a 3G system »

## Slide 51: Generations of mobile telephone systems
1G, analog voice
    AMPS (Advanced Mobile Phone System) is example, deployed from 1980s. Modulation based on FM (as in radio).
2G, analog voice and digital data
    GSM (Global System for Mobile communications) is example, deployed from 1990s. Modulation based on QPSK.
3G, digital voice and data
    UMTS (Universal Mobile Telecommunications System) is example, deployed from 2000s. Modulation based on CDMA
4G, digital data including voice
    LTE (Long Term Evolution) is example, deployed from 2010s. Modulation based on OFDM

## Slide 52: Cellular mobile phone systems
All based on notion of spatial regions called cells
    Each mobile uses a frequency in a cell; moves cause handoff
    Frequencies are reused across non-adjacent cells
    To support more mobiles, smaller cells can be used
Cellular reuse pattern
Smaller cells for dense mobiles

## Slide 53: GSM – Global System for Mobile Communications (1)
  Mobile is divided into handset and SIM card (Subscriber Identity Module) with credentials
  Mobiles tell their HLR (Home Location Register) their current whereabouts for incoming calls
  Cells keep track of visiting mobiles (in the Visitor LR)

## Slide 54: GSM – Global System for Mobile Communications (2)
Air interface is based on FDM channels of 200 KHz divided in an eight-slot TDM frame every 4.615 ms
  Mobile is assigned up- and down-stream slots to use
  Each slot is 148 bits long, gives rate of 27.4 kbps

## Slide 55: UMTS – Universal Mobile Telecommunications System (1)
Architecture is an evolution of GSM; terminology differs
Packets goes to/from the Internet via SGSN/GGSN
Internet

## Slide 56: UMTS – Universal Mobile Telecommunications System (2)
Air interface based on CDMA over 5 MHz channels
  Rates over users <14.4 Mbps (HSPDA) per 5 MHz
  CDMA allows frequency reuse over all cells
  CDMA permits soft handoff (connected to both cells)
Soft
handoff

## Slide 57: Take home
Principal bandwidth limits
  Nyquist’s theorem
CDMA for parallel access
Gray codes to reduce impact of errors for symbols carrying multiple bits of information