## Slide 1: Distributed Systems 5. Data Link Layer
Simon Razniewski
Faculty of Computer Science
Free University of Bozen-Bolzano
A.Y. 2014/2015

## Slide 2: The Data Link Layer
Responsible for delivering frames of information over a single link
  Handles transmission errors and regulates the flow of data
Physical
Link
Network
Transport
Application

## Slide 3: The Data Link Layer
  Framing
  Error Detection and Correction
  Elementary Data Link Protocols
  Sliding Window Protocols
  Example Data Link Protocols

## Slide 4: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Actual data path
Virtual data path
Network
Link
Physical

## Slide 5: Possible Services
Unacknowledged connectionless service
  Frame is sent with no connection / error recovery
  Ethernet is example
Acknowledged connectionless service
  Frame is sent with retransmissions if needed
  Example is 802.11 (WiFi)
Acknowledged connection-oriented service
  Connection is set up; rare

## Slide 6: Why Framing?

## Slide 7: Framing Methods
  Byte count for frames
  Flag bytes with byte stuffing
  Flag bits with bit stuffing
  Physical layer coding violations
    Use non-data symbol to indicate frame

## Slide 8: Framing – Byte count for frames
Frame begins with a count of the number of bytes in it
  Simple, but difficult to resynchronize after an error
Error
case
Expected
case

## Slide 9: Framing – Byte stuffing
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
Stuffing
examples
Frame
format
Need to escape extra ESCAPE bytes too!

## Slide 10: Framing – Bit stuffing
Stuffing done at the bit level:
  Frame flag has six consecutive 1s (not shown)
  On transmit, after five 1s in the data, a 0 is added
  On receive, a 0 after five 1s is deleted
Transmitted bits
with stuffing
Data bits

## Slide 11: Framing – Physical coding violation
How?

## Slide 12: Error Control
Two basic strategies:
Correct errors at receiver side (using error-correcting codes)
Detect errors at receiver side and request retransmission
Preferred method depends on the error probability
  Fiber: Error detection + retransmission
  Wifi: Error correcting codes

## Slide 13: Error Detection and Correction
Error codes add structured redundancy to data so errors can be either detected, or corrected.
Error detection codes:
  Parity
  Checksums
  Cyclic redundancy codes (CRC)
Error correction codes:
  Hamming codes
  Reed-Solomon and Low-Density Parity Check codes
    Mathematically complex, widely used in real systems

## Slide 14: Error Detection – Parity
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110 000  1110 0001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 1110 0101; detected, sum is wrong
  Ex: 3 errors, 1101 1001; detected sum is wrong
  Ex: 2 errors, 1110 1101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½

## Slide 15: Error Detection – Checksums
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: IPv4 protocol uses 16-bit checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Detects random errors with probability 1-(1/2)N
  Vulnerable to systematic errors, e.g., added zeros

## Slide 16: Error Detection – CRCs (1)
Adds bits so that transmitted frame viewed as a polynomial is evenly divisible by a generator polynomial
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible

## Slide 17: Error Detection – CRCs (2)
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits (hardware)
Stronger detection than checksums:
  E.g., can detect all double bit errors
  Not vulnerable to systematic errors

## Slide 18: Richard Hamming (1915-1998)

## Slide 19: Error Bounds – Hamming distance
Code turns data of n bits into codewords of n+k bits
Hamming distance is the minimum bit flips to turn one valid codeword into any other valid one.
  Example with 4 codewords of 10 bits (n=2, k=8):
    0000000000, 0000011111, 1111100000, and 1111111111
    Hamming distance is 5
Bounds for a code with distance:
  2d+1 – can correct d errors (e.g., 2 errors above)
  d+1 – can detect d errors (e.g., 4 errors above)

## Slide 20: Error Correction – Hamming code
Hamming code gives a simple way to add check bits and correct up to a single bit error:
  Check bits are parity over subsets of the codeword
  Recomputing the parity sums (syndrome) gives the position of the error to flip, or 0 if there is no error
  (7,4) Hamming code for (d1,d2,d3,d4,p1,p2,p3)-ordering
p1
d3
p2
p3
d1
d2
d4

## Slide 21
1, 1, 0, 0, 0, 1, 1
0, 0, 1, 0, 1, 1, 1
1, 0, 0, 0, 0, 1, 1
0, 1, 0, 1, 1, 0, 1
1, 1, 0, 0, 0, 1, 1
0, 1, 0, 1, 1, 0, 0
1, 1, 1, 0, 1, 0, 0
0, 0, 1, 0, 1, 1, 1

## Slide 22: Hamming Codes - Generalization
d data bits
r check bits
Values for d and r that satisfy the following equation allow to correct one error:
d+r+1 ≤ 2r

## Slide 23: Error Detection/Control: IBANs
http://www.ibancalculator.com/
Example:
bank code 123456, bank abbreviation WEST
account number 98765432
IBAN: |  | GB82 WEST 1234 5698 7654 32 | 
• Rearrange: |  | W E S T12345698765432 G B82 | 
• Convert to integer (A=10, ..) |  | 3214282912345698765432161182 | 
• Compute remainder: |  | 3214282912345698765432161182 | mod 97 = 1

## Slide 24: Error Control - Preference
Which method is better when?
Example:
  Error probability: 10^-6
  Frame size: 1k bits
  Hamming code to correct one versus parity bit?

## Slide 25: Elementary Data Link Protocols
  Link layer environment »
  Utopian Simplex Protocol »
  Stop-and-Wait Protocol for Error-free channel »
  Stop-and-Wait Protocol for Noisy channel »

## Slide 26: Link layer environment (1)
Commonly implemented as NICs and OS drivers; network layer (IP) is often OS software

## Slide 27: Link layer environment (2)
Link layer protocol implementations use system calls
Group | Library Function | Description
Network layer | from_network_layer(&packet) to_network_layer(&packet) enable_network_layer() disable_network_layer() | Take a packet from network layer to send Deliver a received packet to network layer Let network cause “ready” events Prevent network “ready” events
Physical layer | from_physical_layer(&frame) to_physical_layer(&frame) | Get an incoming frame from physical layer Pass an outgoing frame to physical layer
Events & timers | wait_for_event(&event) start_timer(seq_nr) stop_timer(seq_nr) start_ack_timer() stop_ack_timer() | Wait for a packet / frame / timer event Start a countdown timer running Stop a countdown timer from running Start the ACK countdown timer Stop the ACK countdown timer

## Slide 28: Utopian Simplex Protocol
An optimistic protocol (p1) to get us started
  Assumes no errors, and receiver as fast as sender
  Considers one-way data transfer
  That’s it, no error or flow control …
Sender loops blasting frames
Receiver loops eating frames
}

## Slide 29: Stop-and-Wait – Error-free channel
Protocol (p2) ensures sender can’t outpace receiver:
  Receiver returns a dummy frame (ack) when ready
  Only one frame out at a time – called stop-and-wait
  We added flow control!
Sender waits to for ack after passing frame to physical layer
Receiver sends ack after passing frame to network layer

## Slide 30: Stop-and-Wait – Noisy channel (1)
ARQ (Automatic Repeat reQuest) adds error control
  Receiver acks frames that are correctly delivered
  Sender sets timer and resends frame if no ack)
For correctness, frames and acks must be numbered
  Else receiver can’t tell retransmission (due to lost ack or early timer) from new frame
  For stop-and-wait, 2 numbers (1 bit) are sufficient

## Slide 31: Stop-and-Wait – Noisy channel (2)
Sender loop (p3):
Send frame (or retransmission)
Set timer for retransmission
Wait for ack or timeout
If a good ack then set up for the next frame to send (else the old frame will be retransmitted)
{

## Slide 32: Stop-and-Wait – Noisy channel (3)
Receiver loop (p3):
Wait for a frame
If it’s new then take it and advance expected frame
Ack current frame

## Slide 33: Sliding Window Protocols
  Sliding Window concept »
  One-bit Sliding Window »
  Go-Back-N »
  Selective Repeat »

## Slide 34: Sliding Window concept (1)
Sender maintains window of frames it has sent
  Needs to buffer them for possible retransmission
  Window advances with next acknowledgements
Receiver maintains window of frames it can receive
  Needs to keep buffer space for arrivals
  Window advances with in-order arrivals

## Slide 35: Sliding Window concept (2)
A sliding window advancing at the sender and receiver
  Ex: window size is 1, with a 3-bit sequence number.
At the start
First frame is sent
First frame is received
Sender gets first ack
Sender
Receiver

## Slide 36: Sliding Window concept (3)
Larger windows enable pipelining for efficient link use
  Stop-and-wait (w=1) is inefficient for long links
  Best window (w) depends on bandwidth-delay (BD)
  Want w ≥ 2BD+1 to ensure high link utilization
Pipelining leads to different choices for errors/buffering
  We will consider Go-Back-N and Selective Repeat

## Slide 37: One-Bit Sliding Window (1)
Transfers data in both directions with stop-and-wait
  Piggybacks acks on reverse data frames for efficiency
  Handles transmission errors, flow control, early timers
  Each node is sender and receiver (p4):
. . .
{
Prepare first frame
Launch it, and set timer

## Slide 38: One-Bit Sliding Window (2)
. . .
If a frame with new data then deliver it
Wait for frame or timeout
(Otherwise it was a timeout)
If an ack for last send then prepare for next data frame
Send next data frame or retransmit old one; ack the last data we received

## Slide 39: One-Bit Sliding Window (3)
Interaction example
Time
Notation is (seq, ack, frame number).
Asterisk indicates frame accepted by network layer .

## Slide 40: Go-Back-N
Receiver only accepts/acks frames that arrive in order:
  Discards frames that follow a missing/errored frame
  Sender times out and resends all outstanding frames
Sender
Receiver

## Slide 41: Selective Repeat (1)
Receiver accepts frames anywhere in receive window
  Cumulative ack indicates highest in-order frame
  NAK (negative ack) causes sender retransmission of a missing frame before a timeout resends window
Ack also for frames 2-4

## Slide 42: Selective Repeat (2)
Tradeoff made for Selective Repeat:
  More complex than Go-Back-N due to buffering at receiver
  More efficient use of link bandwidth as only lost frames are resent (with low error rates)
Code in Tanenbaum book

## Slide 43: Example Data Link Protocols
  Packet over SONET »
  PPP (Point-to-Point Protocol) »
  ADSL (Asymmetric Digital Subscriber Loop) »

## Slide 44: Packet over SONET/SDH
Packet over SONET is the method used to carry IP packets over SONET optical fiber links (backbone of Internet)
  Uses PPP (Point-to-Point Protocol) for framing
Protocol stacks
PPP frames may be split over SONET payloads

## Slide 45: PPP
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
  Framing uses a flag (0x7E) and byte stuffing
  “Unnumbered mode” (connectionless unacknow-ledged service) is used to carry IP packets
  Errors are detected with a checksum
IP packet
0x21 for IPv4

## Slide 46: ADSL (1)
Widely used for broadband Internet over local loops
  ADSL runs from modem (customer) to DSLAM (ISP)
  IP packets are sent over PPP and AAL5/ATM (over)

## Slide 47: ADSL (2)
PPP data is sent in AAL5 frames over ATM cells:
  ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
  AAL5 is a format to send packets over ATM
  PPP frame is converted to a AAL5 frame (PPPoA)
AAL5 frame is divided into 48 byte pieces, each of which goes into one ATM cell with 5 header bytes

## Slide 48: Take home
Framing via bit stuffing
Error detection + retransmission versus error correction
  Hamming codes to correct errors
Acknowledgements with sliding windows
Next lecture: Medium access control sublayer