## Slide 1: 7. Network Layer
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service
  Network Layer of the Internet
    IP
    OSPF

## Slide 2: The Network Layer
Responsible for delivering packets between endpoints over multiple links
(Link layer: single link Transport layer: Uses this service)
Physical
Link
Network
Transport
Application

## Slide 3: Design Issues
  Forward packet switching
  Connectionless service – datagrams
  Connection-oriented service – virtual circuits
  Comparison of virtual-circuits and datagrams

## Slide 4: Forward Packet Switching
Hosts send packets into the network; packets are forwarded by routers
ISP’s equipment

## Slide 5: Connectionless Service – Datagrams
Packet is forwarded using destination address inside it
  Different packets may take different paths
ISP’s equipment
A’s table (initially) A’s table (later) C’s Table E’s Table
Dest. Line

## Slide 6: Connection-Oriented – Virtual Circuits
Packet is forwarded along a virtual circuit using tag inside it
  Virtual circuit (VC) is set up ahead of time
ISP’s equipment
A’s table C’s Table E’s Table
In: Line Tag
Line Tag: Out

## Slide 7: Comparison of Virtual-Circuits & Datagrams

## Slide 8: 7. Network Layer
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service
  Network Layer of the Internet
    IP
    OSPF

## Slide 9: Routing Algorithms (1)
  Dijkstra’s Shortest path algorithm
  Flooding
  Distance vector routing
  Link state routing
  Hierarchical routing
  Routing for mobile hosts

## Slide 10: Routing Algorithms (2)
Routing is the process of discovering network paths
  Model the network as a graph of nodes and links
  Decide what to optimize (e.g., fairness vs efficiency)
  Update routes for changes in topology (e.g., failures)
Forwarding is the sending of packets along a path

## Slide 11: Shortest Path Algorithm (1)
Dijkstra’s algorithm computes a sink tree on the graph:
  Each link is assigned a non-negative weight/distance
  Shortest path is the one with lowest total weight
  Using weights of 1 gives paths with fewest hops
Algorithm:
  Start with sink, set distance at other nodes to infinity
  Relax distance to other nodes
  Pick the lowest distance node, add it to sink tree
  Repeat until all nodes are in the sink tree

## Slide 12
Dijkstra(StartingNode A) {
Queue<HashMap<Node,Integer> theQueue;
theQueue.addAll(A.reachableNodesWithDistance);
Integer[] shortestDistances = new Integer[maxNodeCount];
while (theQueue.isNotEmpty()) {
Node nearest = theQueue.removeNearest();
shortestDistances[nearest.id] = nearest.distance;
for (Node n : nearest.reachableNodesWithinDistance) {
int newDistance = nearest.distanceTo(n) + nearest.Distance;
if (!queue.containsKey(n) && shortestDistances[n.id] == null
|| queue.containsKey(n) && queue.get(n)>newDistance)
queue.put(n,newDistance);
}
}
}
N.B.: This is close to java, but the queue likely needs to be implemented as PriorityQueue

## Slide 13: Shortest Path Algorithm (2)
A network and first five steps in computing the shortest paths from A to D. Pink arrows show the sink tree so far.

## Slide 14: Your turn
Shortest paths from A?

## Slide 15: Flooding
A simple method to send a packet to all network nodes
Each node floods a new packet received on an incoming link by sending it out all of the other links
Nodes need to keep track of flooded packets to stop the flood; even using a hop limit can blow up exponentially

## Slide 16: Distance Vector Routing (1)
Distance vector is a distributed routing algorithm
  Shortest path computation is split across nodes
Algorithm:
  Each node knows distance of links to its neighbors
  Each node advertises vector of lowest known distances to all neighbors
  Each node uses received vectors to update its own
  Repeat periodically

## Slide 17: Distance Vector Routing (2)
Network
Vectors received at J from
Neighbors A, I, H and K
New vector for J

## Slide 18: Distance Vector Routing (2)
Network
Vectors received at J from
Neighbors A, I, H and K
New vector for J

## Slide 19: The Count-to-Infinity Problem
Failures can cause DV to “count to infinity” while seeking a path to an unreachable node
Good news of a path to A spreads quickly
X
Bad news of no path to A is learned slowly

## Slide 20: Link State Routing (1)
Link state is an alternative to distance vector
  More computation but simpler dynamics
  Widely used in the Internet (OSPF, IS-IS)
Algorithm:
  Each node floods information about its neighbors in LSPs (Link State Packets); all nodes learn the full network graph
  Each node runs Dijkstra’s algorithm to compute the path to take for each destination

## Slide 21: Link State Routing (2) – LSPs
LSP (Link State Packet) for a node lists neighbors and weights of links to reach them
Network
LSP for each node

## Slide 22: Link State Routing (3) – Reliable Flooding
Seq. number and age are used for reliable flooding
  New LSPs are acknowledged on the lines they are received and sent on all other lines
  Example shows the LSP database at router B

## Slide 23: Hierarchical Routing
Hierarchical routing reduces the work of route computation but may result in slightly longer paths than flat routing
Best choice to reach nodes in 5 except for 5C

## Slide 24: Routing for Mobile Hosts
Mobile hosts can be reached via a home agent
  Fixed home agent tunnels packets to reach the mobile host; reply can optimize path for subsequent packets
  No changes to routers or fixed hosts

## Slide 25
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service
  Network Layer of the Internet
    IP
    OSPF

## Slide 26: Congestion Control (1)
Handling congestion is the responsibility of the Network and Transport layers working together
    We look at the Network portion here
  Traffic-aware routing »
  Admission control »
  Traffic throttling »
  Load shedding »

## Slide 27: Congestion Control (2)
Congestion results when too much traffic is offered; performance degrades due to loss/retransmissions
  Goodput (=useful packets) trails offered load

## Slide 28: Congestion Control (3) – Approaches
Network must do its best with the offered load
  Different approaches at different timescales
  Nodes should also reduce offered load (Transport)

## Slide 29: Traffic-Aware Routing
Choose routes depending on traffic, not just topology
  E.g., use EI for West-to-East traffic if CF is loaded
  But take care to avoid oscillations

## Slide 30: Admission Control
Admission control allows a new traffic load only if the network has sufficient capacity, e.g., with virtual circuits
  Can combine with looking for an uncongested route
Network with some congested nodes
Uncongested portion and route AB around congestion

## Slide 31: Traffic Throttling
Congested routers signal hosts to slow down traffic
  ECN (Explicit Congestion Notification) marks packets and receiver returns signal to sender

## Slide 32: Load Shedding (1)
When all else fails, network will drop packets (shed load)
Can be done end-to-end or link-by-link
Link-by-link (right) produces rapid relief
1
3
2
4
5

## Slide 33: Load Shedding (2)
End-to-end (right) takes longer to have an effect, but can better target the cause of congestion
1
3
2
7
5
6
4

## Slide 34
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service
  Network Layer of the Internet
    IP
    OSPF

## Slide 35: Quality of Service
  Application requirements »
  Traffic shaping »
  Packet scheduling »
  Admission control »
  Integrated services »
  Differentiated services »

## Slide 36: Application Requirements (1)
Different applications care about different properties
  We want all applications to get what they need
.
“High” means a demanding requirement, e.g., low delay

## Slide 37: Application Requirements (2)
Network provides service with different kinds of QoS (Quality of Service) to meet application requirements
Network Service | Application
Constant bit rate | Telephony
Real-time variable bit rate | Videoconferencing
Non-real-time variable bit rate | Streaming a movie
Available bit rate | File transfer
Example of QoS categories from ATM networks

## Slide 38: Traffic Shaping (1)
Traffic shaping regulates the average rate and burstiness of data entering the network
  Lets us make guarantees
Shape traffic here

## Slide 39: Traffic Shaping (2)
Token/Leaky bucket limits both the average rate (R) and short-term burst (B) of traffic
  For token, bucket size is B, water enters at rate R and is removed to send; opposite for leaky.
Leaky bucket
(need not full to send)
Token bucket
(need some water to send)
to send
to send

## Slide 40: Traffic Shaping: Token Bucket
Shaped by R=25 MB/s B=9,6 MB
Shaped by R=25 MB/s B=0 KB
Host traffic
R=25 MB/s B=16 MB
Smaller bucket size delays traffic and reduces burstiness

## Slide 41: Admission Control (1)
Admission control takes a traffic flow specification and decides whether the network can carry it
  Sets up packet scheduling to meet QoS
Example flow specification

## Slide 42: Admission Control (2)
Construction to guarantee bandwidth B and delay D:
  Shape traffic source to a (R, B) token bucket
  Run WFQ with weight W / all weights > R/capacity
  Holds for all traffic patterns, all topologies

## Slide 43
  Design Issues
  Routing Algorithms
    distance vector
    link state routing
  Congestion Control
  Quality of Service
  Network Layer of the Internet
    IP
    OSPF

## Slide 44: Network Layer in the Internet (1)
  IP Version 4
  IP Addresses
  IP Version 6
  Internet Control Protocols
  Label Switching and MPLS
  OSPF—An Interior Gateway Routing Protocol
  BGP—The Exterior Gateway Routing Protocol
  Mobile IP

## Slide 45: Network Layer in the Internet (3)
Internet is an interconnected collection of many networks that is held together by the IP protocol

## Slide 46: IP Version 4 Protocol (1)
IPv4 (Internet Protocol) header is carried on all packets and has fields for the key parts of the protocol:

## Slide 47: Your turn
Given the following header, will the following packet pass a network with an MTU of 1920 bytes?
What will be different if paket is fragmented?

## Slide 48: IP Addresses (1) – Prefixes
Addresses are allocated in blocks called prefixes
  Prefix is determined by the network portion
  Written address/length, e.g., 18.0.31.0/24

## Slide 49: IP Addresses (2) – Subnets
Subnetting splits up IP prefix to help with management
  Looks like a single prefix outside the network
Network divides it into subnets internally
ISP gives network
a single prefix

## Slide 50: IP Addresses (3) – Aggregation
Aggregation joins multiple IP prefixes into a single larger prefix to reduce routing table size
ISP customers have different prefixes
ISP advertises
a single prefix

## Slide 51: IP Addresses (4) – Longest Matching Prefix
Packets are forwarded to the entry with the longest matching prefix or smallest address block
  Complicates forwarding but adds flexibility
Main prefix goes this way
Except for this part!

## Slide 52: IP Addresses (5) – Classful Addresing
Old addresses came in blocks of fixed size (A, B, C)
  Carries size as part of address, but lacks flexibility
  Called classful (vs. classless) addressing

## Slide 53: IP Addresses (6) – NAT
NAT (Network Address Translation) box maps one external IP address to many internal IP addresses
  Uses TCP/UDP port to tell connections apart
  Violates layering; very common in homes, etc.

## Slide 54: Your turn
Computer A has the IPv4 address (including the subnet mask in CIDR notation) 141.89.228.65/26.
Computer B is reachable as 141.89.228.63/26.
Do they belong to the same subnet?

## Slide 55: IP Version 6 (1)
Major upgrade in the 1990s due to impending address exhaustion, with various other goals:
    Support billions of hosts
    Reduce routing table size
    Simplify protocol
    Better security
    Attention to type of service
    Aid multicasting
    Roaming host without changing address
    Allow future protocol evolution
    Permit coexistence of old, new protocols, …
Deployment has been slow & painful, but may pick up pace now that addresses are all but exhausted

## Slide 56
Three hundred and forty undecillion, two hundred and eighty-two decillion, three hundred and sixty-six nonillion, nine hundred and twenty octillion, nine hundred and thirty-eight septillion, four hundred and sixty-three sextillion, four hundred and sixty-three quintillion, three hundred and seventy-four quadrillion, six hundred and seven trillion, four hundred and thirty-one billion, seven hundred and sixty-eight million, two hundred and eleven thousand, four hundred and fifty-six.

## Slide 57: IP Version 6 (2 )
IPv6 protocol header has much longer addresses (128 vs. 32 bits) and is simpler (by using extension headers)

## Slide 58: IP Version 6 (3)
IPv6 extension headers handles other functionality

## Slide 59: Internet Control Protocols (1)
IP works with the help of several control protocols:
  ICMP is a companion to IP that returns error info
    Required, and used in many ways, e.g., for traceroute
  ARP finds Ethernet address of a local IP address
    Glue that is needed to send any IP packets
    Host queries an address and the owner replies
  DHCP assigns a local IP address to a host
    Gets host started by automatically configuring it
    Host sends request to server, which grants a lease

## Slide 60: Internet Control Protocols (2)
Main ICMP (Internet Control Message Protocol) types:

## Slide 61: Internet Control Protocols (3)
ARP (Address Resolution Protocol) lets nodes find target Ethernet addresses [pink] from their IP addresses

## Slide 62: Label Switching and MPLS (1)
MPLS (Multi-Protocol Label Switching) sends packets along established paths; ISPs can use for QoS
  Path indicated with label below the IP layer

## Slide 63: Label Switching and MPLS (2)
Label added based on IP address on entering an MPLS network (e.g., ISP) and removed when leaving it
  Forwarding only uses label inside MPLS network

## Slide 64: OSPF— Interior Routing Protocol (1)
OSPF computes routes for a single network (e.g., ISP)
  Models network as a graph of weighted edges
Network:
Graph:
Broadcast LAN modeled as a well-connected node
3

## Slide 65: OSPF— Interior Routing Protocol (2)
OSPF divides one large network (Autonomous System) into areas connected to a backbone area
  Helps to scale; summaries go over area borders

## Slide 66: OSPF— Interior Routing Protocol (3)
OSPF (Open Shortest Path First) is link-state routing:
  Uses messages below to reliably flood topology
  Then runs Dijkstra to compute routes

## Slide 67: BGP— Exterior Routing Protocol (1)
BGP (Border Gateway Protocol) computes routes across interconnected, autonomous networks
  Key role is to respect networks’ policy constraints
Example policy constraints:
    No commercial traffic for educational network
    Never put Iraq on route starting at Pentagon
    Choose cheaper network
    Choose better performing network
    Don’t go from Apple to Google to Apple

## Slide 68: BGP— Exterior Routing Protocol (2)
Common policy distinction is transit vs. peering:
  Transit carries traffic for pay; peers for mutual benefit
  AS1 carries AS2↔AS4 (Transit) but not AS3 (Peer)

## Slide 69: BGP— Exterior Routing Protocol (3)
BGP propagates messages along policy-compliant routes
  Message has prefix, AS path (to detect loops) and next-hop IP (to send over the local network)

## Slide 70: Mobile IP
Mobile hosts can be reached at fixed IP via a home agent
  Home agent tunnels packets to reach the mobile host; reply can optimize path for subsequent packets
  No changes to routers or fixed hosts

## Slide 71: Take home
IP-Addresses: NETID+HOSTID
Routing
  Distance vector
    Problem: Count to infinity
  Link state
    Challenge: Information propagation
Internet
  OSPF inside a network
  BGP between networks